RCC TF 56_009

Test Cases for RCS 5.1 NNI

v 1.0

17 Apr 2013

This is a Draft Non Binding Permanent Reference Document of the GSMA

.

Security Classification – NON CONFIDENTIAL GSMA MATERIAL

Copyright Notice

Copyright © 2013 GSM Association

Antitrust Notice

The information contain herein is in full compliance with the GSM Association’s antitrust compliance policy.

1.	Introduction	6

1.1	Functional assumptions	6

1.2	Testing Environment Assumptions	6

1.3	Assumed architecture	6

1.4	References	6

1.5	Acronyms	7

2.	Introduction and Overall IMS NNI Architecture	9

2.1	Configuration and registration	9

2.2	Roaming	9

2.3	Legacy	9

3.	Capability Discovery	10

3.1	SIP OPTIONS based	10

3.1.1	Pre-call capability discovery	10

3.1.2	In-call/in-session capability discovery	14

3.1.3	Multi-device handling	14

3.1.4	Exception conditions	14

3.2	Presence based	15

3.2.1	User Discovery	15

3.2.2	Capability Update	18

3.2.3	Multidevice handling	19

3.2.4	Feature Interaction	20

3.2.5	Exception conditions	22

4.	IP Interconnection	23

5.	Social Presence	24

5.1	Buddy List Management	24

5.2	VIP/non-VIP	28

5.3	SPI Attribute Management	30

5.4	Location Management	33

5.5	Multidevice handling	35

6.	File Transfer	37

6.1	File Transfer using MSRP	37

6.1.1	Basic File Transfer (MSRP)	37

6.1.2	Multi-device handling	47

6.1.3	Exception conditions	49

6.2   File transfer using HTTP	52

6.2.1  Basic File Transfer (http)	52

6.2.2  Multidevice handling	60

6.2.3  Exception conditions	62

7.	Messaging	68

7.1	Standalone Messaging	68

7.1.1	Message Processing	68

7.1.2	Multi-device Handling	71

7.1.3	Exception Conditions	74

7.2	1-to-1 Chat	75

7.2.1	Session Management	75

7.2.2	Message Handling	86

7.2.3	Multi-device Handling	90

7.2.4	Exception Conditions	92

7.3	Group Chat	92

7.3.1	Session Management	92

7.3.2	Message Handling	108

7.3.3	Multi-device Handling	108

7.3.4	Exception Conditions	108

8.	Content Sharing	110

8.1	Video Share	110

8.1.1	Basic Video Share	110

8.1.2	Multiparty call and Video Share	114

8.1.3	Call on hold and Video Share	116

8.1.4	Call waiting and Video Share	119

8.1.5	Multi-device handling	119

8.1.6	Exception conditions	121

8.2	Image Share	126

8.2.1	Basic Image Share	126

8.2.2	Multiparty call and Image Share	128

8.2.3	Call on hold and Image Share	130

8.2.4	Multi-device handling	130

8.2.5	Exception conditions	132

9.	IP Voice and Video Call	137

9.1	IP Voice Call	137

9.1.1	Two-party IP Voice Call over NNI	137

9.1.2	Multi-party RCS Voice Call over NNI	146

9.2	IP Video call	148

9.2.1	Two-party IP Video call over NNI	148

9.2.2	Multi-party RCS Video call over NNI	162

10.	Personal Network Blacklist	163

10.1	Standalone Message	163

10.1.1	Standalone message (Pager Mode) is screened out in terminating network	163

10.1.2	Standalone message (Large Message Mode) is screened out in terminating network	164

10.2	Chat Session	165

10.2.1	Chat (1-to-1) invitation is screened out in terminating network	165

10.3	File Transfer	166

10.3.1	File Transfer invitation is screened out in terminating network	166

11.	Document Management	167

11.1	Document History	167

11.2	Other Information	168

# Introduction

## Functional assumptions

Users A, B, C and D belong to different operators/service providers

- all users have been provisioned in their respective network.

- all users’ telephones have been configured unless otherwise specified.

- all users are registered in their RCS networks unless otherwise specified. The registration timer for each user is far from expiration.

- all users are in 3G/LTE mobile coverage unless otherwise specified. WiFi coverage is specified explicitly.

## Testing Environment Assumptions

All users’ operators have successfully verified RCS implementations, including UNI, in their respective networks.

ENUMs and DNSes have been established and provisioned if applicable.

All users use UEs of their operator’s choice.

Repeat the test swapping the role of the devices

Tests are performed as applicable by subscriber and terminal capabilities.

It is assumed that the following testing over NNI has been concluded prior to execution of RCS 5.1 NNI Test Cases (see also RCS 5.1 NNI spreadsheet, Annex A to IR.90):

- IP connectivity

- SIP connectivity

- RCS media connectivity

- addressing and routing, including ENUM and DNS functionality

## Assumed architecture

Reference to IR.65 for IMS Interconnect architecture

## References

| Document Number | Title |
| --- | --- |
| [3GPP TS 26.114] | IP Multimedia Subsystem (IMS); Multimedia Telephony; Media handling and interaction |
| [3GPP TS 24.173] | IMS Multimedia telephony communication service and supplementary services; Stage 3 |
| [3GPP TS 24.229] | IP multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP); Stage 3 |
| [3GPP TS 24.610] | Communication HOLD (HOLD) using IP Multimedia (IM) Core Network (CN) subsystem; Protocol specification |
| [ITU H.264] | Advanced video coding for generic audiovisual services |
| [GSMA IR.65] | IMS Roaming and Interworking Guidelines v6.0 |
| [GSMA IR.74] | Video Share Interoperability Specification v1.4 |
| [GSMA IR.79] | Image Share Interoperability Specification v1.4 |
| [GSMA IR.90] | RCS Interworking Guidelines v4.0 |
| [GSMA RCS5.1] | Rich Communication Suite 5.1 Advanced Communications, Services and Client Specification v1.0 |

## Acronyms

| Acronym / Abbreviation | Description |
| --- | --- |
| BPEF | Blacklist Enforcement Function |
| CPM | Converged IP Messaging |
| CS | Circuit Switched |
| DNS | Domain Name System |
| EAB | Enhanced Address Book |
| ENUM | E.164 Number Mapping |
| GSMA | GSM Association |
| HSPA | High Speed Packet Access |
| HTTP | Hyper-Text Transfer Protocol |
| IP | Internet Protocol |
| IPX | Internet Protocol Packet Exchange |
| LTE | Long Term Evolution |
| MSRP | Message Session Relay Protocol |
| NAT | Network Address Translation |
| NNI | Network-to-Network Interface |
| OMA | Open Mobile Alliance |
| PNB | Personal Network Blacklist |
| RCS-AA | RCS Access Agnostic mode |
| RCS-CS | RCS CS mode |
| RTP | Real Time Protocol |
| SPI | Social Presence Information |
| UE | User Equipment |
| UX | User Experience |
| VIP | Very Important Person |
| VoHSPA | Voice over HSPA |
| VoLTE | Voice over LTE |

# Introduction and Overall IMS NNI Architecture

## Configuration and registration

N/A

## Roaming

N/A

## Legacy

N/A

# Capability Discovery

## SIP OPTIONS based

### Pre-call capability discovery

| Test case ID | RCS_3_1_1_1 |
| --- | --- |
| Related Test Cases |  |
| Feature tested | Capability discovery, SIP OPTIONS based |
| Purpose | Initial check of capabilities between A and B |
| Pre-conditions Scenario |  |
| Test procedure | A initiates Capability Discovery with B |
| Expected results Post-conditions | A’s device shows B’s correct capabilities |
| Deep inspection | 1) Verify OPTIONS exchange with correct service capability tags |

| Test case ID | RCS_3_1_1_2 |
| --- | --- |
| Related test cases |  |
| Tested feature |  |
| Purpose | Capability Discovery with non IMS enabled, non-RCS B |
| Pre-conditions Scenario | B is non IMS enabled and non-RCS capable |
| Test procedure | 1) A initiates Capability Discovery with B |
| Expected results Post-conditions | B’s capabilities displayed in A’s device remain unchanged |
| Deep inspection | 1) Verify 404 NOT FOUND response |

| Test case ID | RCS_3_1_1_3 |
| --- | --- |
| Related test cases |  |
| Tested feature |  |
| Purpose | Capability Discovery with IMS enabled, non-RCS B |
| Pre-conditions Scenario | B is non IMS enabled and non-RCS capable |
| Test procedure | 1) A initiates Capability Discovery with B |
| Expected results Post-conditions | B’s capabilities displayed in A’s device remains unchanged |
| Deep inspection | 1) Verify 404 NOT FOUND response |

| Test case ID | RCS_3_1_1_4 |
| --- | --- |
| Related test cases |  |
| Tested feature |  |
| Purpose | Capability exchange with RCS-capable B which is not registered in IMS |
| Pre-conditions Scenario | 1) B is an RCS user who is currently not registered in IMS 2) IM CAP ALWAYS ON and FT CAP ALWAYS ON are not enabled on A |
| Test procedure | 1) A selects B 2) Capability exchange takes place but the network reports that B is offline |
| Expected results Post-conditions | B’s capabilities are not available to A |
| Deep inspection | 1) Verify OPTIONS exchange 2) Verify response from the IMS core is 480 (TEMPORARILY UNAVAILABLE) |

| Test case ID | RCS_3_1_1_5 |
| --- | --- |
| Related test cases |  |
| Tested feature |  |
| Purpose | Capability exchange with RCS-capable B which has just lost connectivity but remains registered in IMS (e.g. suddenly removing battery from their device) |
| Pre-conditions Scenario | 1) B loses connectivity but remains registered in IMS (e.g. suddenly removing battery from their device) 2) IM CAP ALWAYS ON and FT CAP ALWAYS ON are not enabled on A |
| Test procedure | 1) A selects B 2) Capability exchange takes place |
| Expected results Post-conditions | B’s capabilities are not available to A since the network reports that B is offline. |
| Deep inspection | 1) Verify OPTIONS exchange 2) Verify that the response from the IMS core is 408 (REQUEST TIMEOUT) or 487 (REQUEST TERMINATED) |

### In-call/in-session capability discovery

No tests

### Multi-device handling

No tests

### Exception conditions

| Test case ID | RCS_3_1_4_1 |
| --- | --- |
| Related test cases |  |
| Tested feature |  |
| Purpose | Capability query in 1-1 chat (file transfer no longer available due to 2G coverage) |
| Pre-conditions Scenario | A and B are engaged in a 1-1 chat FT CAP ALWAYS ON is not set on A |
| Test procedure | 1) B moves to 2G coverage 2) That triggers a capability exchange started from B to update A about the fact FT is no longer supported |
| Expected results Post-conditions | FT is not available to the user (greyed out) based on step #2 (Test procedure) |
| Deep inspection | 1) Verify OPTIONS exchange with correct service capability tags 2) Verify response from the core is 200 OK |

| Test case ID | RCS_3_1_4_2 |
| --- | --- |
| Related test cases |  |
| Tested feature |  |
| Purpose | Capability query in 1-1 chat (file transfer becomes available) |
| Pre-conditions Scenario | B is under 2G coverage Both Are in a RCS 1-1 chat FT CAP ALWAYS ON is not set on A |
| Test procedure | 1) B moves to 3G/HSPA coverage 2) That triggers a capability exchange started from B to update A about the fact FT is supported |
| Expected results Post-conditions | FT is shown as available |
| Deep inspection | 1) Verify OPTIONS exchange with correct service capability tags 2) Verify response from the core is 200 OK |

## Presence based

### User Discovery

| Test case ID | RCS_3_2_1 _1 |
| --- | --- |
| Related Test Cases |  |
| Feature tested | Presence Based User Discovery |
| Purpose | User Discovery: Device First time registration |
| Pre-conditions Scenario | CAPABILITY DISCOVERY MECHANISM = PRESENCE Optional CAPABILITY POLLING is supported by the operator B and C are contacts in A’s EAB; both are registered and available A has not yet initially registered in her service provider’s network |
| Test procedure | A performs first time registration and configuration |
| Expected results Post-conditions | Resulting NOTIFY messages at the NNI contain the appropriate service descriptions. The amount of time it takes to get the information for contacts in the address book is a function of operator policy and device implementation After some period of time, A’s EAB correctly displays that B and C are RCS contacts. |
| Deep inspection | Anonymous SUBSCRIBE is seen over the NNI for each contact that is RCS capable that is in a foreign /NNI domain Resulting NOTIFY messages at the NNI contain the appropriate service descriptions. |

| Test case ID | RCS_3_2_1_2 |
| --- | --- |
| Related Test Cases | RCS_3_2_1 _1 |
| Feature tested | Presence Based User Discovery |
| Purpose | User Discovery: Registered non-RCS Contact Added to EAB |
| Pre-conditions Scenario | B is a non-RCS user, not in A’s EAB, registered in IMS B is not presence enabled |
| Test procedure | A adds B in her EAB |
| Expected results Post-conditions | A’s EAB indicates B is not an RCS User A can still communicate with B using other services as appropriate |
| Deep inspection | In the case where there is IMS peering between carriers for services other than RCS, an anonymous SUBSCRIBE may be sent over the NNI, but it is expected that an error code of some sort would be returned; there would normally not be a NOTIFY. If user B is in a network with a presence server, it is likely that if a NOTIFY is returned it would not contain any RCS service descriptions. It is possible, but not likely, that the remote non-RCS domain would support anonymous operations. |

| Test case ID | RCS_3_2_1_3 |
| --- | --- |
| Related Test Cases | RCS_3_2_1 _1 |
| Feature tested | Presence Based User Discovery |
| Purpose | User Discovery: Not Registered RCS Contact Added to EAB |
| Pre-conditions Scenario | B is a provisioned RCS user, not in A’s EAB, not registered in IMS (e.g. all devices powered off) |
| Test procedure | A adds B in her EAB |
| Expected results Post-conditions | A’s EAB indicates B is an RCS User A’s EAB indicates that B’s has no specific service capabilities available |
| Deep inspection | Anonymous SUBSCRIBE is seen over the NNI from A for B Resulting NOTIFY messages to A at the NNI contain no service descriptions because User B has no active devices registered This assumes that no services are defined using permanent presence mechanisms |

### Capability Update

| Test case ID | RCS_3_2_2_1 |
| --- | --- |
| Related Test Cases |  |
| Feature tested | Presence Based Capability Update |
| Purpose | Capability Update: User interacts with RCS contact |
| Pre-conditions Scenario | A and B are registered RCS users |
| Test procedure | B interacts with A in their EAB B’s device performs a capability update fetch. As capability information is updated on B’s device |
| Expected results Post-conditions | A’s current capability information is correctly displayed in B’s EAB |
| Deep inspection | Device B sends an anonymous SUBSCRIBE over NNI to A The resulting notify routed back to B accurately characterizes the service availability based on operator service and network connection status, policy, and device status. |

| Test case ID | RCS_3_2_2_2 |
| --- | --- |
| Related Test Cases |  |
| Feature tested | Presence Based Capability Update |
| Purpose | Operator has service availability policy that is contingent upon device network / attachment status |
| Pre-conditions Scenario | Operator has a service availability policy that is contingent upon network connectivity type and status Device B implements such a policy for a specific service for presence based Capability discovery/Capability Update. |
| Test procedure | Device B is in network coverage / attachment state that, per operator policy and device capabilities, publishes that one or more services are available. The device may also publish service descriptions that are provided independent of network coverage / attachment state. A performs capability update fetch B’s capability changes - (i.e. she changes network coverage / attachment status such that on ore more services are impacted. A performs capability update fetch |
| Expected results Post-conditions | For the first fetch, A’s capability information indicates the set of network dependent services that properly reflect device B’s status and operator policy. For the second fetch, A’s network attachment status has changed, one or more services are impacted, and thus A’s capability information now indicates the changed set of services that properly reflect device B’s status and operator policy. |
| Deep inspection | Each fetch results in a notify being generated that accurately characterizes the service availability for each user based on operator service and network connection status policy and device status. The cause of the differences in the service information provided between the first and second fetch is that in between the two fetches: Device B network/attachment status changed Device B published the changed set of services to their Presence Server Note that neither of these vents are visible at the NNI, but if they do not both occur no change will be detected between the two fetches. |

### Multidevice handling

| Test case ID | RCS_3_2_3_1 |
| --- | --- |
| Related Test Cases |  |
| Feature tested | Presence Based Capability Discovery – Multidevice Handling |
| Purpose | User Discovery: Registered RCS Contact with multiple registered devices added to EAB |
| Pre-conditions Scenario | CAPABILITY DISCOVERY MECHANISM = PRESENCE B is a provisioned RCS user, not in A’s EAB, and is registered in IMS B has multiple RCS devices registered and active in the network |
| Test procedure | A adds B in her EAB |
| Expected results Post-conditions | A’s EAB correctly displays that B is an RCS user and display B’s relevant capability information. The information shows the services available across all of B’s devices |
| Deep inspection | Anonymous SUBSCRIBE seen at NNI from User A to User B Resulting NOTIFY message at the NNI contains the appropriate service descriptions. Since B has two or more devices online and publishing at the time of the fetch, the NOTIFY message for that user contains the composed presence information for all devices. This service information is composed contingent upon standards based composition policy as well as operator specific policy as applicable. |

### Feature Interaction

| Test case ID | RCS_3_2_4_1 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2 |
| Feature tested | Presence Based Capability Discovery – Feature Interaction |
| Purpose | User Capability & Social Presence Information (SPI) Service Interaction |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A is sharing Social Presence Information with B. (RCS_5_1_1) |
| Test procedure | B interacts with A. This could be in any form including an incoming call, messaging interface, or interaction at the EAB. |
| Expected results Post-conditions | B’s device does not perform capability update fetches. If A is a VIP buddy, then B immediately and always sees A’s current capability information. Changes in SPI information status are sent automatically to B and are available for display. (RCS_5_2_1) If B is a non-VIP buddy then a non VIP SPI fetch will be performed by B’s device. (RCS_5_2_2) |
| Deep inspection | 1. Anonymous fetches are not seen across the NNI for SPI contacts. |

| Test case ID | RCS_3_2_4_2 |
| --- | --- |
| Related Test Cases | RCS_5_1_1 |
| Feature tested | Presence Based Capability Discovery – Feature Interaction |
| Purpose | SPI Who Can I Invite? RCS Contact /Capability Discover Interaction |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A is not sharing Social Presence Information with B. B is RCS and social presence information sharing capable. |
| Test procedure | A interacts with contact B. A’s EAB shows B can be invited to share RCS SPI. A may now choose to invites B to share RCS SPI (make them an RCS buddy). |
| Expected results Post-conditions | A can see which contacts are RCS users capable of sharing SPI, and is able to invite them to do so. |
| Deep inspection | A sends anonymous subscribe over NNI for B Resulting NOTIFY contains the feature tag for SPI. |

| Test case ID | RCS_3_2_4_3 |
| --- | --- |
| Related Test Cases | RCS_5_1_1 |
| Feature tested | Presence Based Capability Discovery – Feature Interaction |
| Purpose | SIP OPTIONS and Presence Based capabilities interaction based on common device stack client (as defined 2.6.1.3.2 of RCC.07) |
| Pre-conditions Scenario | CAPABILITY DISCOVERY MECHANISM = PRESENCE Optional CAPABILITY POLLING is supported by the operator A CAPABILITY DISCOVERY VIA COMMON STACK =1 B is a contact in A’s EAB. B is in a network that does not support presence based capabilities discovery (SIP OPTIONS only supported) A has not yet initially registered in her service provider’s network |
| Test procedure | A performs first time registration and configuration |
| Expected results Post-conditions | A’s device displays the appropriate service information for contact B |
| Deep inspection | Anonymous SUBSCRIBE is seen over the NNI for contact B . Contact B’s network responds to the SUBSCRIBE with a 405 or a 501. The client A understands that these specific codes indicate that the specified contact requires SIP OPTIONS. The client A performs a SIP OPTIONS exchange and displays the results to User A. NOTE: This will not work for an anonymous SUBSCRIBE that was generated by an RLS unless the PS and device have defined a specific RLMI resource state that uniquely identifies list members for which these specific error codes have been received. These values should probably be defined and normalized in the RCS UNI spec. |

### Exception conditions

| Test case ID | RCS_3_2_5_1 |
| --- | --- |
| Related Test Cases |  |
| Feature tested | Presence Based Capability Discovery – Feature Interaction |
| Purpose | User Capability: RCS Feature Tag Recognized, Not Supported |
| Pre-conditions Scenario | B’s service provider supports an RCS feature not supported by A’s service provider. |
| Test procedure | A performs an action triggering an update of her contact’s user capability information (e.g. she interacts with the contact) |
| Expected results Post-conditions | B’s capability information is retrieved, including a service description that is not recognized or not supported by A’s service provider. B’s relevant capability information is correctly displayed in A’s EAB. The unsupported service is ignored and not advertised to User A. |
| Deep inspection | A generates a anonymous subscribe over the NNI to B. The resulting s notify from B accurately characterizes the service availability based on operator service and network connection status policy and device status. If both operators only use the same RCS services, or if any service filtering mechanism is used to strip such descriptions from the NOTIFY before it is routed over the NNI, then this is not testable. |

# IP Interconnection

No tests (see General Assumptions)

# Social Presence

## Buddy List Management

| Test case ID | RCS_5_1_1 |
| --- | --- |
| Related Test Cases | RCS_5_1_2, RCS_5_1_3, RCS_5_1_4, RCS_5_1_5, RCS_5_1_6, RCS_3_2_4_2 |
| Feature tested | Social Presence Buddy List Management |
| Purpose | Social Presence: Sharing Invitation Accept |
| Pre-conditions Scenario | Social Presence enabled for both A and B via Presence Server (PRESENCE PROFILE = 1) Both devices have active buddy list A and B are not in each other’s buddy lists (they are not already buddies) User B has not blocked User A User A can see that User B supports SPI ( Who Can I invite – test RCS_3_2_4_2) |
| Test procedure | A invites B to share social presence information B receives the social presence information sharing invitation and accepts |
| Expected results Post-conditions | Subsequent to the B accepting As buddy request: A and B can see each other’s Social Presence Information |
| Deep inspection | A SIP SUBSCRIBE will be sent from A to B over NNI Response to SUBSCRIBE is 202 Accepted. This will be followed by a “dummy” NOTIFY with a pending subscription state After User B accepts the invite: There will be a full NOTIFY from B to A with an active subscription state, This notify will contain USER B’s SPI info. User B network will send a SUBSCRIBE over NNI which will result in 200 OK and NOTIFY for active subscription with User A SPI info. |

| Test case ID | RCS_5_1_2 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_1_3, RCS_5_1_4, RCS_5_1_5, RCS_5_1_6 |
| Feature tested | Social Presence Buddy List Management |
| Purpose | Social Presence: Sharing Invitation Ignore |
| Pre-conditions Scenario | Social Presence enabled for both A and B via Presence Server (PRESENCE PROFILE = 1) Both devices have active buddy list and winfo subscriptions A and B are not in each other’s buddy lists (they are not already buddies) User B has not blocked User A |
| Test procedure | A invites B to share social presence information B receives the social presence information sharing invitation and ignores it A sees state as pending until B accepts, blocks, or timeout occurs. |
| Expected results Post-conditions | B receives an indication that the invitation has not been accepted A and B are not able to see each other’s Social Presence Information |
| Deep inspection | A SIP SUBSCRIBE will be sent from A to B over NNI Response to SUBSCRIBE is 202 Accepted. This will be followed by a “dummy” NOTIFY with a pending subscription state |

| Test case ID | RCS_5_1_3 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_1_2, RCS_5_1_4, RCS_5_1_5, RCS_5_1_6 |
| Feature tested | Social Presence Buddy List Management |
| Purpose | Social Presence: Sharing Invitation Blocked |
| Pre-conditions Scenario | Social Presence enabled for both A and B via Presence Server (PRESENCE PROFILE = 1) Both devices have active buddy list and winfo subscriptions A and B are not in each other’s buddy lists (they are not already buddies) B has not blocked User A |
| Test procedure | A invites B to share social presence information B blocks the social presence information sharing invitation A again invites B to share social presence information B does not get another sharing invitation (User A is in blocked-contacts) |
| Expected results Post-conditions | A does receive an indication that the invitations was being Blocked (status terminated/rejected). B does not receive A’s social presence information sharing invitations subsequent to blocking B. A and B are not able to see each other’s Social Presence Information B does not see any subsequent invites from B to share presence information |
| Deep inspection | A SIP SUBSCRIBE will be sent from A to B over NNI Response to SUBSCRIBE is 202 Accepted. This will be followed by a “dummy” NOTIFY with a pending subscription state After User B blocks the invite there will be a NOTIFY from B to A with an terminated, rejected subscription state. This notify will not contain USER B’s SPI info. Any subsequent SUBSCRIBE from A will result in a NOTIFY with terminated, rejected subscriptions state. |

| Test case ID | RCS_5_1_4 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_1_2, RCS_5_1_3, RCS_5_1_5, RCS_5_1_6 |
| Feature tested | Social Presence Buddy List Management |
| Purpose | Social Presence: Sharing Invitation Unblocked |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) Both devices have active buddy list and winfo subscriptions B has blocked A’s Social Presence Invitations (test RCS_5_1_1) B is not currently in A’s buddy list |
| Test procedure | B unblocks A. A invites B to share social presence information B receives the social presence information sharing invitation and accepts |
| Expected results Post-conditions | Subsequent to the B accepting As buddy request: A and B can see each other’s Social Presence Information |
| Deep inspection | Deep inspection is same for the accept case as defined in test RCS_5_1_1 |

| Test case ID | RCS_5_1_5 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_1_2, RCS_5_1_3, RCS_5_1_4, RCS_5_1_6 |
| Feature tested | Social Presence Buddy List Management |
| Purpose | Social Presence: Sharing Revoked |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) Both devices have active buddy list and winfo subscriptions A and B are sharing Social Presence Information (test RCS_5_1_1) A and B can each see each other’s Social Presence Information |
| Test procedure | A revokes social presence information sharing with B. |
| Expected results Post-conditions | A no longer sees B’s social presence information in the EAB. B no longer sees A’s social presence information in the EAB. B can see that the relationship was revoked B’s contact information (e.g. vCard) remains in A’s address book. |
| Deep inspection | Subsequent to A placing B in the revoked contact list, B’s network will issue a SIP SUBSCRIBE for B that has an expires time of “0” to close the subscription. Bs network will respond with a NOTIFY with a subscription state of terminated. A User network will issue a NOTIFY to the existing SUBSCRIBE from B to A with a subscription state of terminated, rejected. As a result, the active subscriptions in both directions have been terminated. |

| Test case ID | RCS_5_1_6 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_1_2, RCS_5_1_3 |
| Feature tested | Social Presence Buddy List Management |
| Purpose | Social Presence: Personalized Invitation |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) Both devices have active buddy list and winfo subscriptions A is not a contact in B’s EAB. A and B are not in each other’s buddy lists (they are not already buddies) B has not blocked User A |
| Test procedure | A defines a Nickname at their UE A sends an invitation (with the nickname) to B to share SPI from that UE. |
| Expected results Post-conditions | User B receives the social presence information sharing invitation. Since User A is not defined in B’s local address book, the initiation to share presence information should use the nickname defined by User A (This is not visible at NNI but validates that User B received and UE uses it properly) |
| Deep inspection | The A user defined nickname is included as part of the identity information provided in the “P-Preferred-Identity” and “From” header of the SIP SUBSCRIBE request from A to B. |

## VIP/non-VIP

| Test case ID | RCS_5_2_1 |
| --- | --- |
| Related Test Cases | RCS_5_1_1 |
| Feature tested | Social Presence: VIP Subscription over NNI. |
| Purpose | This demonstrates that information can be obtained over NNI for VIP contacts using long-lived subscriptions that can be refreshed and maintained as appropriate |
| Pre-conditions Scenario | A and B are sharing Social Presence Information. (test RCS_5_1_1) A and Bs devices are on the network, initialized, and have active subscriptions to their VIP lists Operator policy and device configuration supports refreshing VIP subscriptions. |
| Test procedure | A and B can see each other’s SPI . Each user makes changes to one or more SPI attributes. The expires time used for the VIP subscription expires Each user makes changes to one or more SPI attributes. |
| Expected results Post-conditions | A and B can see the updates to SPI information After the expires time, A and B can see updates to SPI information |
| Deep inspection | VIP list information is propagated using long lived subscriptions. At the NNI, individual long lived subscriptions should be seen for each watcher/presentity. When any user makes changes to SPI information, a NOTIFY should be seen at the NNI which contains the latest SPI information. Watchers/RLS should refresh subscriptions before they expire so that users do not detect and interruption in VIP SPI service. Thus, prior to any individual SUBSCRIBE reaching its expires time, the RLS should send a refresh SUBSCRIBE over the NNI to maintain the subscription in the active state. This does not specify variations that may be seen contingent upon any optimizations that may be in use over the NNI including condition notifications, filtering, notification suppression, or throttling. |

| Test case ID | RCS_5_2_2 |
| --- | --- |
| Related Test Cases | RCS_5_1_1 |
| Feature tested | Social Presence: non-VIP Subscription over NNI. |
| Pre-conditions Scenario | A and B are sharing Social Presence Information. (test RCS_5_1_1) A and B are non-VIP contacts with each other. |
| Test procedure | In order to get updated information for a non VIP contact, the user must interact with a VIP contact in one form or another. For example, A interacts with B on the local EAB. |
| Expected results Post-conditions | This interaction with the non-VIP contact will trigger an SPI fetch from A to B which will get B’s SPI and service information. A can see B’s SPI information |
| Deep inspection | Non- VIP list information is obtained using fetch subscriptions. At the NNI, individual anonymous fetch subscription should be seen from A to B A NOTIFY will be sent from B to A over the NNI; the NOTIFY contains B’s SPI information |

## SPI Attribute Management

| Test case ID | RCS_5_3_1 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2 |
| Feature tested | Social Presence: SPI attribute management |
| Purpose | Social Presence: Availability changed from Unavailable to Available |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) Availability is enabled (AVAILABILITY AUTHORIZATION = 1) A and B are sharing Social Presence Information. (test RCS_5_1_1) A and B are VIP contacts A has defined their availability status to “unavailable” |
| Test procedure | A changes her availability from Unavailable to Available. |
| Expected results Post-conditions | B sees A’s status as Available. After A changes het availability status from Available to Unavailable, this information is displayed to User B Both A & B can originate communications and receive communications (i.e. availability status does not impact communications capability). Note: the Availability status is informative. Even if a user is noted as Unavailable, communication with that can still be initiated. |
| Deep inspection | When A changes availability status, a NOTIFY is sent from A to B over NNI that contains the new information. |

| Test case ID | RCS_5_3_2 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2 |
| Feature tested | Social Presence: SPI attribute management |
| Purpose | Social Presence: Portrait Icon Change |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A and B are sharing Social Presence Information. (test RCS_5_1_1) A and B are VIP contacts A has defined a portrait icon |
| Test procedure | A changes her portrait icon. |
| Expected results Post-conditions | B sees A’s portrait icon. After A changes their icon, B sees A’s new portrait icon. |
| Deep inspection | When A changes their icon, a NOTIFY is sent from A to B over NNI that contains the link to the icon which resides in the Presence Content XDMS of A’s operator. B device must detect change of link, and perform XCAP GET to retrieve updated icon via transaction with local domain XCAP Root URI - this is not visible at the NNI. The inter-network Proxy of User B will forward the HTTP GET from B over the HTTP NNI point that is addressed to the inter-network proxy of User A’s XDMS. The GET at the NNI will result in a 200 OK that contains the updated icon as a MIME attachment which will be forwarded to B for display. |

| Test case ID | RCS_5_3_3 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2 |
| Feature tested | Social Presence: SPI attribute management |
| Purpose | Social Presence: Free Text Change |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A and B are sharing Social Presence Information. (test RCS_5_1_1) A and B are VIP contacts A has defined Free Text |
| Test procedure | A changes her Free Text |
| Expected results Post-conditions | B sees A’s free text. After A changes their free text, B sees A’s updated free text |
| Deep inspection | When A changes free text, a NOTIFY is sent from A to B over NNI that contains the new information. |

| Test case ID | RCS_5_3_4 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2 |
| Feature tested | Social Presence: SPI attribute management |
| Purpose | Social Presence: Favorite Link and label Change |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A and B are sharing Social Presence Information. (test RCS_5_1_1) A and B are VIP contacts A has defined Favorite link and label |
| Test procedure | A sets/changes her Favourite Link and label info |
| Expected results Post-conditions | B sees A’s Favourite Link and label info. After A changes their Favourite Link and label info, B sees A’s updated Favourite Link and label info |
| Deep inspection | When A changes availability status, a NOTIFY is sent from A to B over NNI that contains the new information. Note/Example values:. A wants to share her blog with friends. She fills in the URL with www.userA_blog.com and fills in the label with “Pizza Party Photos”. |

## Location Management

| Test case ID | RCS_5_4_1 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2 |
| Feature tested | Social Presence: Location management |
| Purpose | Geolocation Declaritive text and location sharing policy management; authorize and revoke |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A is sharing Social Presence Information with Users B and C. (test RCS_5_1_1) Band C are in the same network. Users A, B, and C are VIP contacts None of the users have authorized location sharing |
| Test procedure | A sets her declarative text location manually, e.g. “I’m in Austin, Texas.” A enables location sharing with B After some period of time (after verifying B has seen location information) A revokes location sharing information with B. |
| Expected results Post-conditions | A’s location information is not visible to B or C After A enables location sharing with B, B can see the declarative text information A’s location information is not visible to C A cannot see the location of B or C (not symmetrical) After A revokes location sharing with B, B can no longer see the declarative text information A’s location information is not visible to B or C |
| Deep inspection | When A changes location policy allowing B, a NOTIFY is sent from A to B over NNI that contains the new information. Any subsequent NOTIFY to C do not contain location information. When A changes location policy revoking B, a NOTIFY is sent from A to B over NNI that in which the location information has been removed. Any NOTIFY to C do not contain location information. Note: The mechanisms where A defines location privacy policy is at the UNI/HTTP over Ut and is not visible at the NNI. Location information shouldn’t appear for any watcher over the NNI until the appropriate policy has been defined by the user at their XDMS. |

| Test case ID | RCS_5_4_2 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2, RCS_5_4_1 |
| Feature tested | Social Presence: Location management |
| Purpose | Social Presence: Coordinate information Provided |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A is sharing Social Presence Information with B, including location (test RCS_5_1_1) |
| Test procedure | A defines her map location (e.g. adds a pin to a map). A removes her map locations (removes/deletes pin from a map) |
| Expected results Post-conditions | A’s map location is displayed in B’s map display. A’s map location is cleared from B’s EAB map display. |
| Deep inspection | When A defines location information a NOTIFY is sent from A to B over NNI that contains the new information. When A removes location information a NOTIFY is sent from A to B over NNI from which the location information has been removed. |

| Test case ID | RCS_5_4_3 |
| --- | --- |
| Related Test Cases | RCS_5_1_1, RCS_5_2_1, RCS_5_2_2, RCS_5_4_1 |
| Feature tested | Social Presence: Location management |
| Purpose | Social Presence: Location – Time Zone |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) A is sharing Social Presence Information with B, including location (test RCS_5_1_1) Both operators support Time Zone, and devices under test support Time Zone and the time zone has been defined for A & B A & B are VIP contacts |
| Test procedure | A and B examine their SPI information for each other |
| Expected results Post-conditions | A and B can see each other Time Zone. |
| Deep inspection | The NOTIFY messages between A and B will contain Time Zone information. If either A or B changes their time zone – whether this is user or device driven - a NOTIFY will be generated which identifies the new Time Zone information. |

## Multidevice handling

| Test case ID | RCS_5_5_1 |
| --- | --- |
| Related Tests | RCS_5_1_1 |
| Feature tested | Social Presence: Multidevice Handling |
| Purpose | Social Presence: Interaction – Multidevice Invitation |
| Pre-conditions Scenario | Social Presence enabled via Presence Server (PRESENCE PROFILE = 1) B has multiple devices (e.g. mobile and PC) A is not sharing social presence information with B. |
| Test procedure | A sends a social presence invitation to B. B receives the invitation on all of her devices. B accepts the invitation on one of her devices |
| Expected results Post-conditions | The invitation to share Social Information is shown on all of B’s devices B can accept the invitation on any device, and then receive A’s SPI on all of her devices. |
| Deep inspection | A SIP SUBSCRIBE will be sent from A to B over NNI Response to SUBSCRIBE is 202 Accepted. This will be followed by a “dummy” NOTIFY with a pending subscription state After User B accepts the invite: There will be a full NOTIFY from B to A with an active subscription state, This notify will contain USER B’s SPI info. User B network will send a SUBSCRIBE over NNI which will result in 200 OK and NOTIFY for active subscription with User A SPI info. There will be a SUBSCRIBE for each of B’s active devices over the NNI for B’s information. |

# File Transfer

## File Transfer using MSRP

### Basic File Transfer (MSRP)

| Test case ID | RCS_6_1_1_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Successful file transfer (single file with single recipient) |
| Pre-conditions Scenario | A and B are File Transfer capable A has B as RCS contact. B has enough free storage space to receive file. File size being transferred is smaller than the warning file size. |
| Test procedure | A selects one file from the local storage and then selects the file transfer option. A selects B from the list of active RCS contacts and selects to share. B reviews and then accepts the invitation. 4. The file is transferred to B. |
| Expected results Post-conditions | RCS capability exchange takes place and A sees that file transfer is available for each recipient. B receives file transfer invitation Including the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). Upon B accepting the file transfer invitation, the file is transferred and received by B. B can access the file |
| Deep inspection | 1) Verify capability exchange 2) Verify file transfer invitation process 3) Verify file transfer session establishment 4) Verify successful transfer completion and session termination |

| Test case ID | RCS_6_1_1_2 |
| --- | --- |
| Related test cases | RCS_6_1_1_1 |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Successful multiple file transfers (multiple files to single recipient) |
| Pre-conditions Scenario | A has B as RCS contact. B has enough free storage space to receive file(s). File size being transferred is smaller than the warning file size. |
| Test procedure | A selects three files from the local storage and then selects the file transfer option. A selects B from the list of active RCS contacts and selects to share. B reviews and then accepts the invitation. The files are transferred to B. |
| Expected results Post-conditions | RCS capability exchange takes place and A sees that file transfer is available for each recipient. For each file, the following steps can be verified: B receives file transfer invitation. B should see the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). Upon B accepting the file transfer invitation, the file is transferred and received by B. |
| Deep inspection | 1) Verify capability exchange2) Verify that the sessions are NOT established in parallel to avoid UX impact 3) For each session: 3.a) Verify file transfer invitation process 3.b) Verify file transfer session establishment 3.c) Verify successful transfer completion and session termination |

| Test case ID | RCS_6_1_1_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Successful file transfer (single file with multiple recipients using conference focus) |
| Pre-conditions Scenario | A has Users B, C and D as RCS contacts. All users have enough free storage space to receive file. File size being transferred is smaller than the warning file size |
| Test procedure | A selects one file from the local storage and then selects the file transfer option. A selects B, C and D from the list of active RCS contacts and selects to share. B, C and D review and then accept the invitation. The file is transferred to B, C and D. |
| Expected results Post-conditions | For each user, the following steps can be verified: At step 2 A sees that file transfer is available for each recipient. At step 3, the recipient receives file transfer invitation. The recipient should see the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). At step 4, upon the recipient accepting the file transfer invitation, the file is transferred and received. At step 4, the recipient can access the file (e.g., from storage on the handset). |
| Deep inspection | 2) Verify that only ONE session is established from the sender to conference focus and one terminating session to each recipient from the focus 3) For each terminating session: 3.a) Verify file transfer invitation process 3.b) Verify file transfer session establishment 3.c) Verify successful transfer completion and session termination |

| Test case ID | RCS_6_1_1_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Successful multiple file transfer (multiple files to multiple recipients) |
| Pre-conditions Scenario | A has B and C as RCS contacts. All users have enough free storage space to receive file(s). File size being transferred is smaller than the warning file size. A, B and C are in an active group chat session |
| Test procedure | A selects three files from the local storage and then selects the file transfer option. A selects B and C from the list of contacts and selects to share. B and C review and then accept the invitation. The files are transferred to B and C |
| Expected results Post-conditions | For each user, the following steps can be verified: RCS capability exchange takes place and A sees that file transfer is available for each recipient. For each file, the following steps can be verified: The recipient receives file transfer invitation. The recipient should see the size of the file and an indication of the file type (e.g., MIME icon or mini-preview). Upon the recipient accepting the file transfer invitation, the file is transferred and received. The recipient can access the file |
| Deep inspection | 1) Verify that only ONE session is established from the sender and one terminating session to each recipient 2) For each terminating session: 2.a) Verify file transfer invitation process 2.b) Verify file transfer session establishment 2.c) Verify successful transfer completion and session termination |

| Test case ID | RCS_6_1_1_5 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Successful simultaneous sessions, one for file transfer one for chat. |
| Pre-conditions Scenario | A has B and C as RCS contacts. All users have enough free storage space to receive file(s). File size being transferred is smaller than the warning file size. A, B and C are in an active group chat session |
| Test procedure | 1. A selects file transfer option 2. A selects one file, and select share option 3. B accepts the invitation and opens the files 4. B send IM/Chat invitation to A 5. A accepts IM/Chat invitation 6. IM/Chat session starts |
| Expected results Post-conditions | 3a. B receives files 3b. B can open the files properly 4. A receives IM/Chat invitation 5. IM/Chat session established For A->B leg verify: 1) B receives the invitation stating the file type and the size 2) If it is a supported file type, B should visualize the relevant MIME icon or mini-preview should be displayed within the chat window (all FT take place on a chat window) 3) A can progress the transfer in the notification bar (the transfer does not block the UI) 4) B receives file 5) B can open the file properly |
| Deep inspection | 1) Verify capabililty exchange2) For file transfer session: 2.a) Verify file transfer invitation process; FT session is separate from chat sessions 2.b) Verify file transfer session establishment 2.c) Verify successful transfer completion and session termination |

| Test case ID | RCS_6_1_1_6 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Verifies correct operation when file transfer is rejected |
| Pre-conditions Scenario | A has B as RCS contacts. File size being transferred is smaller than the warning file size. |
| Test procedure | 1) A selects one file from the local storage and then selects the file transfer option. 2) A selects B from the list of active RCS contacts and selects to share. 3) B rejects the invitation. |
| Expected results Post-conditions | B receives the file transfer invitation. The file is not received by B. A is notified that B has rejected the file transfer request. |
| Deep inspection | 1 ) Verify capability exchange 2) Verify file transfer invitation process 3) Verify file transfer session is not established with an error code 603 Decline response |

| Test case ID | RCS_6_1_1_7 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Successful auto-accept of the file transfer session (fast acceptance) |
| Pre-conditions Scenario | 1) Capabilities exchange has taken place confirming file transfer share is possible 2) ftAutAccept parameter on B client is set to 1 |
| Test procedure | 1. A selects B 2. A selects file transfer option 3. A selects one file and select share option |
| Expected results Post-conditions | 1) B receives file 2) B can open the file correctly |
| Deep inspection | 1) Verify capability exchange 2) Verify file transfer invitation auto-accept 3) Verify file transfer session establishment 4) Verify successful transfer completion and session termination |

| Test case ID | RCS_6_1_1_8 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Ongoing file transfer cancelled by the sender |
| Pre-conditions Scenario | 1) All users have enough free storage space to receive file/s |
| Test procedure | 1. A selects B 2. A selects file transfer option 3. A selects a file 4. B accepts the invitation 5. A cancels file transfer |
| Expected results Post-conditions | 3a. B receives files invitation 5a. A cancelled file transfer; B receives error message, |
| Deep inspection | 1) Verify file transfer invitation process 2) Verify file transfer session establishment 3) Verify cancelation and session termination with a SIP BYE from A |

| Test case ID | RCS_6_1_1_9 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Ongoing File transfer cancelled by the recipient |
| Pre-conditions Scenario | 1) All users have enough free storage space to receive file/s |
| Test procedure | 1. A selects a contact from his/her address book 2. A selects file transfer option 3. A selects a file4. B accepts the invitation 5. B cancels file transference while third file is being transferred. |
| Expected results Post-conditions | 3a. B receives files invitation 4a. B receives first and second file 5a. A receives error message, B cancelled file transference. 5b. B can open received files properly (1st and 2nd) |
| Deep inspection | 1) Verify capability exchange 2) Verify file transfer invitation process 3) Verify file transfer session establishment 4) Verify cancelation and session termination with a SIP BYE from B before 3rd file is completely transferred |

| Test case ID | RCS_6_1_1_10 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Unsuccessful transfer: recipient does not answer |
| Pre-conditions Scenario | B has auto-accept disabled All users have enough free storage space to receive file/s |
| Test procedure | 1. A selects B 2. A selects file transfer option 3. A selects a file 4. B does NOT answer the file transfer invitation |
| Expected results Post-conditions | 1. B receives file invitation 2. A receives an error message after timeout |
| Deep inspection | 1 Verify capability exchange 2) Verify file transfer invitation process 3) Verify SIP INVITE timeout |

| Test Case ID | RCS_6_1_1_11 |
| --- | --- |
| Related Test Cases | RCS_6_1_1_12 |
| Feature Tested | File Transfer; File Transfer using MSRP |
| Purpose | Interrupted file transfer resumed by recipient |
| Pre-conditions Scenario | A and B are capable for RCS MSRP-based file transfer A and B are shown as available A and B use manual acceptance of file transfer |
| Test procedure | A sends a file to B (Note: send a large file to allow interrupted during file transfer) B accepts the invitation and file transfer starts During transferring, the file transfer is interrupted (e.g. A or B loses connection momentarily or network problem) B resumes the file transfer |
| Expected results Post-conditions | When B detects the file transfer has been interrupted and resumes the file transfer, A receives a file transfer invitation from B (Note: The resume strategy is Service Provider policies- such as how quick the resume will be initiated, how many retry, etc. Based on error code) If A client supports file transfer resume, A accepts the invitation and the file transfer is resumed from where it was interrupted B receives the entire file If A client does not support file transfer resume, A client rejects the invitation A is informed of the file transfer failure |
| Deep inspection | Verify that A receives a SIP INVITE from B for resume includes the file-range attribute including the file-selector for the missing part Verify that if A does not support resume, the SIP INVITE for the resume from B is rejected. |

| Test Case ID | RCS_6_1_1_12 |
| --- | --- |
| Related Test Cases | RCS_6_1_1_11 |
| Feature Tested | File Transfer; File Transfer using MSRP |
| Purpose | Interrupted file transfer resumed by sender |
| Pre-conditions Scenario | A and B are capable for RCS MSRP-based file transfer A and B are shown as available A and B use manual acceptance of file transfer |
| Test procedure | A sends a file to B (Note: send a large file to allow interrupted during file transfer) B accepts the invitation and file transfer starts During transferring, the file transfer is interrupted (e.g. A or B loses connection momentarily or network problem) A resumes the file |
| Expected results Post-conditions | When A detects the file transfer has been interrupted and resumes the file transfer, B receives a file transfer invitation from A (Note: The resume strategy is Service Provider policies- such as how quick the resume will be initiated, how many retry, etc. Based on error code) If B client supports file transfer resume, B accepts the invitation and return 200 OK with SDP including the correct file-range attribute with file selector attribute The file transfer is resumed from where it was interrupted B receives the entire file successfully If B client does not support file transfer resume, B client rejects the invitation A may be informed of the file transfer failure (UI implementation) |
| Deep inspection | Verify that B receives the SIP INVITE from A for resume includes the best estimated file-range attribute and the file-selector attribute for the missing part Verify that B responds 200 OK to the resume INVITE with a correct file-range attribute and file selector attribute Verify that if B does not support resume, the SIP INVITE for the resume from A is rejected |

### Multi-device handling

| Test Case ID | RCS_6_1_2_1 |
| --- | --- |
| Related Test Cases | RCS_6_1_1_11, RCS_6_1_1_12 |
| Feature Tested | File Transfer; File Transfer using MSRP |
| Purpose | File transfer resume request sent to the device that originates the file transfer (Multi-device Handling) |
| Pre-conditions Scenario | A and B are capable for RCS MSRP-based file transfer A and B are shown as available A and B use manual acceptance of file transfer A and B clients supports file transfer resume A has 2 device A1 and A2. Both A1 and A2 are online. |
| Test procedure | A1 sends a file to B (Note: send a large file to allow interrupted during file transfer) B accepts the invitation and file transfer starts During transferring, the file transfer is interrupted (e.g. A1 or B loses connection momentarily or network problem) B resumes the file |
| Expected results Post-conditions | When B detects the file transfer has been interrupted and resumes the file transfer, A1 receives a file transfer invitation from B When A1 accept the invitation, A1 resumes the file transfer B receives the file successfully |
| Deep inspection | Verify that the device identifier (sip.instance or GRUU) is included in the SIP INVITE for the original file transfer from A1 to B Verify that the same device identifier is used to address the sender in the SIP INVITE of the resume request from B Verify that A1 receives the SIP INVITE from B for resume If the device identifier is not included in the original file transfer SIP INVITE from A1 to B, no device identifier will then be included in the SIP INVITE of the resume request from B. The resume SIP INVITE will be forked to A1 and A2. A1 will answer the SIP INVITE with 200 OK |

### Exception conditions

| Test case ID | RCS_6_1_3_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Unsuccessful transfer before completion: Sender loses coverage |
| Pre-conditions Scenario | 1) All users have enough free storage space to receive file/s |
| Test procedure | 1. A selects B 2. A selects file transfer option 3. A selects two files and selects share option 4. B accepts the invitation 5. A loses coverage while third file is being transferred. |
| Expected results Post-conditions | 3a. B receives files invitation 4a. B receives first and second file 5a. B receives error message, A has interrupted file transfer 5b. B receives updated capabilities for A 5c. B can open received files properly (1st and 2nd) |
| Deep inspection | 1) Verify capability exchange 2) Verify file transfer invitation process 3) Verify file transfer session establishment 4) Verify session timeout?? |

| Test case ID | RCS_6_1_3_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Unsuccessful transfer before completion: Recipient loses coverage |
| Pre-conditions Scenario | 1) All users have enough free storage space to receive file/s |
| Test procedure | 1. A selects B 2. A selects file transfer option 3. A selects two files and selects share option 4. B accepts the invitation 5. B loses coverage while third file is being transferred. |
| Expected results Post-conditions | 3a. B receives files invitation 4a. B receives first and second file 5a. A receives error message, B has interrupted file transference 5b. A receives updated capabilities for B 5c. B can open received files properly (1st and 2nd) |
| Deep inspection | 1) Verify capability exchange 2) Verify file transfer invitation process 3) Verify file transfer session establishment 4) Verify session timeout |

| Test case ID | RCS_6_1_3_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | File size warning limit (terminating side) (for NNI testing, ensure File Transfer file size attribute is carried over NNI and available to B to invoke FT warning procedures) |
| Pre-conditions Scenario | 1) Capabilities exchange between A and B has taken place confirming file transfer is possible 2) FT AUT ACCEPT on B is set to 1 3) FT WARN SIZE in KB on B is set to a value below the size of the file to be sent 4) FT MAX SIZE in KB on both A and B is set to a value above the size of the file to be sent |
| Test procedure | 1) A selects a file to share with B that is larger than the FT WARN SIZE for B, but smaller than the FT MAX SIZE on both A and B. |
| Expected results Post-conditions | 1) A gets a warning message if the FT WARN SIZE parameter is also configured for A and confirmation is asked to proceed 2) A confirms and proceeds 3) Instead of B’s device auto-accepting the file, B is receives the file size and is asked to accept the File Transfer invitation 4) After about 5 seconds, B accepts the File Transfer invitation |
| Deep inspection | 1) Verify file transfer invitation process 2) Verify that B was asked to accept the invitation because the file size was greater than the FT WARN SIZE and no auto-accept observed |

| Test case ID | RCS_6_1_3_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using MSRP |
| Purpose | Maximum File size exceeded (terminating side) (for NNI testing, ensure File Transfer file size attribute is carried over NNI and available to B’s network to invoke FT maximum size exceeded procedures) |
| Pre-conditions Scenario | 1) Capabilities exchange between A and B has taken place confirming file transfer is possible 2) FT MAX SIZE in KB on A is greater than FT MAX SIZE in KB on B |
| Test procedure | 1) A select a file to send to B that is smaller than the FT MAX SIZE on A but larger than the FT MAX SIZE on B. |
| Expected results Post-conditions | 1) B detects that the file to be transferred is too big (i.e., a=file-selector size value is larger than FT MAX SIZE on B), so B answers the INVITE with a 488 “Not Acceptable Here” and warning header set to “133 Size exceeded”, or 2) Network B’s Messaging Server detects that the file exceeds the maximum file transfer size and returns an error a 403 “Forbidden” and warning header set to “133 Size exceeded”. |
| Deep inspection | 1) Verify the a=file-selector size attribute in the incoming SIP request. 2) If B detects that the file to be transferred is too big (i.e., a=file-selector size value is larger than FT MAX SIZE on B), verify that B answers the INVITE with a 488 “Not Acceptable Here” and warning header set to “133 Size exceeded”. 3) If Network B’s Messaging Server detects that the file exceeds the maximum file transfer size verify that it returns an error a 403 “Forbidden” and warning header set to “133 Size exceeded”. |

## 6.2   File transfer using HTTP

### 6.2.1  Basic File Transfer (http)

For the following test cases a HTTP proxy on the recipient side and a dedicated link (e.g. VPN) between operators are assumed, so that http traffic will also be considered as NNI traffic.

Note: If this is not the case, the http traffic is not seen on the NNI and therefore not part of the deep inspection of the test case.

| Test Case ID | RCS_6_2_1_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in active one-to-one chat |
| Pre-conditions Scenario | 1. A and B are in active 1-2-1 chat session. 2. B has enough free storage space to receive file. 3. File size being transferred is smaller than the warning file size. 4. Clients A and B support HTTP-based FT according to former capability exchange. 5. A, B parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. |
| Test procedure | 1. A selects one file from the local storage and then selects the file transfer option. 2. B receives and accepts the file download notification if prompted. 3. B opens the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipient. 2. B receives file transfer download notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received. The recipient can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A. |
| Deep inspection | 1. Verify that capability exchange including HTTP FT tag occurs before chat session setup. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that FT notification XML is sent inside the active chat. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Verify that HTTPS requests for file and optional thumbnail are sent to the content server in A's network and the content is received. 6. Verify display notification in SIP MESSAGE. Note: It is assumed that the file is always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in new one-to-one chat |
| Pre-conditions Scenario | 1. A has B as RCS contact. 2. A and B are not in active 1-2-1 chat session. 3. B has enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A and B support HTTP-based FT. 6. A parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. 7. B parameters: FT MAX SIZE is same for A, B. Preferred File Transfer technology is HTTP. Standalone message enabled is set to false. |
| Test procedure | 1. A selects one file from the local storage and then selects the file transfer option. 2. A selects B and selects to share. 3. B receives and accepts the chat invitation and file download notification if prompted. 4. B opens the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipient. 2. B receives file transfer download notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received. The recipient can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A. |
| Deep inspection | 1. Verify that capability exchange including HTTP FT tag but without standalone message capability occurs before chat session setup. 2. Verify that a new 1-2-1 chat session is created carrying the http FT tag in the accept contact header and used to send the FT notification to B. 3. Verify support of FT HTTP xml content type during SDP negotiation. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Verify that HTTPS requests for file and optional thumbnail are sent to the content server in A's network and the content is received. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in 1-2-1 standalone message |
| Pre-conditions Scenario | 1. A has B as RCS contact. 2. A and B are not in active 1-2-1 chat session 3. B has enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A and B support HTTP-based FT and standalone messaging. 6. A, B parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. Standalone message enabled is set to true. |
| Test procedure | 1. A selects one file from the local storage and then selects the file transfer option.^ 2. A selects B and selects to share. 3. B receives and accepts the file download notification if prompted. 4. B opens the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipient. 2. B receives file transfer download notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received. The recipient can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A. |
| Deep inspection | 1. Verify that capability exchange including HTTP FT and standalone message tags occurs before FT. 2. Verify that a the FT notification XML is sent in a standalone message. 3. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 4. Verify that HTTPS requests for file and optional thumbnail are sent to the content server on A's network and content is received. 5. Verify display notification in SIP MESSAGE. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful one to many HTTP-based file transfer in active group chat (GC focus on A side) |
| Pre-conditions Scenario | 1. A, B, and C are in active group chat session. 2. Group chat is hosted by MNO A side. 3. B, C have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A, B, and C support HTTP-based FT. 6. FT MAX SIZE is the same for A, B, C. 7. A parameters: Preferred File Transfer technology is HTTP File transfer in group chat is supported. 8. B,C parameters: Preferred File Transfer technology is HTTP |
| Test procedure | A selects one file from the local storage and starts file transfer to the group chat. B, C receive and accept the file download notification. B, C open the file. |
| Expected results Post-conditions | 1. A sees that file transfer is available. 2. Users B, C receive the file download notification and see the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received by B, C. The recipients can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A for delivery to B and C. |
| Deep inspection | 1. Verify capability exchange during session setup including HTTP FT tag in contact header within SIP INVITE and 200 OK between GC focus A and clients B, C. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that the FT notification XML is sent inside the active chat from to clients B, C . 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Verify that HTTPS requests for file and optional thumbnail are sent by B and C to content server in A's network and the content is received. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_5 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in active group chat (GC focus on B side) |
| Pre-conditions Scenario | 1. A, B, and C are in active group chat session 2. Group chat is hosted by MNO B side. 3. B, C have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A, B, and C support HTTP-based FT 6. A, C parameters: FT MAX SIZE is the same as for A, B, C. Preferred File Transfer technology is HTTP. 7. B parameters: FT MAX SIZE is the same for A, B, C. Preferred File Transfer technology is HTTP. File transfer in group chat is supported. |
| Test procedure | A selects one file from the local storage and starts file transfer to the group chat. B, C receive and accept the file download notification if prompted. B, C open the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipients B, C. 2. Users B, C receive the file download notification and see the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received by B, C. The recipients can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A for delivery to B and C |
| Deep inspection | 1. Verify capability exchange during session setup including HTTP FT tag in contact header within SIP INVITE and 200 OK between client A, C and GC focus server B. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that the FT notification XML is sent inside the active chat from to clients B, C. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Verify that HTTPS requests for file and optional thumbnail are sent by B, C to content server A and the content is received. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_6 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in new group chat (GC focus on A side) |
| Pre-conditions Scenario | 1. A has users B, C as RCS contacts. 2. A, B, C are in not in an active group chat session. 3. B, C have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size 5. Clients A, B, and C support HTTP-based FT. 6. A parameters: FT MAX SIZE is the same for A, B, C Preferred File Transfer technology is HTTP. Standalone message enabled is set to false. File transfer in group chat is supported. 7. B, C parameters: FT MAX SIZE is the same for A, B, C. Preferred File Transfer technology is HTTP. Standalone message enabled is set to false (for B or C). |
| Test procedure | A selects one file from the local storage and then selects the file transfer option. A selects users B, C and selects to share. B, C receive and accept the group chat invitation and file download notification if prompted. B, C open the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipients B, C. 2. Users B, C receives file download notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received by B, C. The recipients can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A for delivery to B and C. |
| Deep inspection | 1. Verify that capability exchange including FT HTTP tag but without standalone message tag for A, B, or C occurs before file transfer. 2. Verify capability exchange during session setup including HTTP FT tag in contact header within SIP INVITE and 200 OK between GC focus and clients B, C . 3. Verify support of FT HTTP xml content type during SDP negotiation 4. Verify that a new chat is created and used to send the file transfer notification to clients B, C. 5. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 6. Verify that chat session is closed afterwards. 7. Verify that HTTPS requests for file and optional thumbnail are sent by B and C to content server in A's network and the content is received. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_7 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in 1-N standalone message |
| Pre-conditions Scenario | 1. A has users B, C as RCS contacts. 2. A, B, C are in not in an active group chat session. 3. B, C have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A, B, and C support HTTP-based FT and standalone messaging. 6. A,B,C parameters: FT MAX SIZE is the same for A, B, C. Preferred File Transfer technology is HTTP. File transfer in group chat is supported. Standalone message enabled is set to true. |
| Test procedure | A selects one file from the local storage and then selects the file transfer option. A selects Users B, C and selects to share. Users B, C receive and accept the file download notification if prompted. B, C open the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipients B, C. 2. Users B, C receive file download notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received by B, C. The recipients can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A for delivery to B and C. |
| Deep inspection | 1. Verify that capability exchange including HTTP FT and standalone message tags between clients A, B, C occurs. 2. Verify that the FT notification is sent in a standalone message to B, C. 3. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 4. Verify that HTTPS requests for file and optional thumbnail are sent by B and C to content server in A's network and content is received. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_1_8 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in active one-to-one chat (resume file download) |
| Pre-conditions Scenario | 1. A and B are in active 1-2-1 chat session. 2. B has enough free storage space to receive file. 3. File size being transferred is smaller than the warning file size 4. Clients A and B support HTTP-based FT. 5. A parameters: FT MAX SIZE is same for A, B. Preferred File Transfer technology is HTTP. File Transfer Resume supported is set to true. 6. B parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. |
| Test procedure | A selects one file from the local storage and then selects the file transfer option to B. B receives and accepts the file download notification if prompted. The file transfer to B is started. During file download B gets out of coverage. B resumes download when returning to coverage. B opens the file. |
| Expected results Post-conditions | 1. A sees that file transfer is available for the recipient. 2. B receives file transfer notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The download of the file starts but stops before the transfer is complete. 4. When back in data coverage, the transfer proceeds until the file received by B. 5. Display notification is received and shown on client A (sent by B). |
| Deep inspection | 1. Verify that capability exchange including HTTP FT tag occurs before chat session. 2. Verify support of FT HTTP xml content type during SDP negotiation 3. Verify that FT notification XML is sent inside the active chat. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Verify that HTTPS requests for file and optional thumbnail are sent to content server in As network and first content is received. 6. Verify that HTTPS requests for file is resumed and not restarted when client gets back in coverage. 7. Verify display notification in SIP MESSAGE. Note: It is assumed that the file will always be uploaded successfully. |

### 6.2.2  Multidevice handling

| Test Case ID | RCS_6_2_2_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Successful HTTP-based file transfer in active one-to-one chat with multiple clients on A side. |
| Pre-conditions Scenario | 1. User A has two registered and online clients A1 and A2. 1. A1 and B are in active 1-2-1 chat session. 2. B has enough free storage space to receive file. 3. File size being transferred is smaller than the warning file size. 4. Clients A1, A2 and B support HTTP-based FT according to former capability exchange. 5. Network A, B NNI parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. |
| Test procedure | 1. A1 selects one file from the local storage and then selects the file transfer option. 2. B receives and accepts the file download notification if prompted. 3. B opens the file. |
| Expected results Post-conditions | 1. A1 sees that file transfer option is available for the recipient B. 3. B receives file transfer notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 4. The file is transferred and received by B. 5. Display notification is received and shown only on client A1 but not on client A2. |
| Deep inspection | 1. Verify that capability exchange including HTTP FT tag occurs before chat session. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that FT notification XML is sent inside the active chat. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Verify that HTTPS requests for file and optional thumbnail are sent to content server on A's network and content is received. 6. Verify display notification in SIP MESSAGE. The accept-contact header shall address the device id (sip.instance or GRUU) of client A1 out of the contact header during session setup. Note: It is assumed that the file will always be uploaded successfully. |

### 6.2.3 Exception conditions

| Test Case ID | RCS_6_2_3_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Fallback to MSRP-based file transfer (one-to-many) due to missing GC focus support |
| Pre-conditions Scenario | 1. A, B, and C are in active group chat session. 2. Group chat is hosted by MNO B side and focus does not support http based FT. 3. B, C have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A, B, and C support HTTP-based FT. 6. A,C parameters: FT MAX SIZE is the same as for A, B, C. Preferred File Transfer technology is HTTP. File Transfer Thumbnail supported. 7. Network B NNI parameters: FT MAX SIZE is the same for A, B, C. Preferred File Transfer technology is MSRP. File Transfer Thumbnail supported. File transfer in group chat is not supported. |
| Test procedure | A selects one file from the local storage and starts file transfer to the group chat. B, C receive and accepts the file transfer invitation if prompted. B, C open the file. |
| Expected results Post-conditions | 1. A sees that file transfer is available for the group chat. 2. Users B, C receive the file transfer invitation and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. The file is transferred and received by B, C sequentially. The recipients can access the file (e.g., from storage on the handset). 4. Display notification is received and shown on client A for delivery to B and C |
| Deep inspection | 1. Verify that capability exchange including FT, FT thumb tags occurs between clients A, B, C before chat session. 2. Verify capability exchange during session setup without HTTP FT tag in contact header within SIP INVITE and 200 OK between client GC focus server B and client A. 3. Verify that 2 additional MSRP sessions are created and used to send the file to B and C 4. Verify that the 2 MSRP sessions are closed afterwards. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_3_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Partially successful HTTP-based file transfer in active group chat (one client does not support HTTP-based FT) |
| Pre-conditions Scenario | 1. A, B, and C are in active group chat session. 2. Group chat is hosted by MNO A side. 3. B, C have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A, B support HTTP-based FT, client C supports MSRP-based FT only. 6. A, B parameters: FT MAX SIZE is the same for A, B, C. Preferred File Transfer technology is HTTP. File transfer in group chat is supported. 7. C parameters: FT MAX SIZE same as for A. Preferred File Transfer technology is MSRP. |
| Test procedure | A selects one file from the local storage and starts file transfer to the group chat. B receives and accepts the file download notification if prompted. B opens the file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipients B, C. 3. Users B receives file transfer download notification and sees the size of the file and an indication of the file type (e.g. MIME icon or mini-preview). 3. Users C does not receive the file transfer invitation. 4. The file is transferred and received by B. The recipient can access the file (e.g., from storage on the handset). 5. Display notification is received and shown on client A for delivery to B only |
| Deep inspection | 1. Verify capability exchange during session setup in contact header within SIP INVITE and 200 OK between GC focus A and clients B, C. GC focus A and clients A, B shall include HTTP FT tag. Client C shall include FT, FT thumb tags. 2. Verify support of FT HTTP xml content type during SDP negotiation by GC focus and clients A, B. 3. Verify that the FT notification XML is sent inside the active chat to client B only. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org 5. Verify that HTTPS requests for file and optional thumbnail are sent by B to content server on A's network and content is received. 6. Verify display notification in SIP MESSAGE is received from client B. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_3_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Unsuccessful HTTP-based file transfer in new one-to-one chat (validity expired) |
| Pre-conditions Scenario | 1. A has B as RCS contact. 2. A and B are not in active 1-2-1 chat session. 3. B have enough free storage space to receive file. 4. File size being transferred is smaller than the warning file size. 5. Clients A and B support HTTP-based FT. 6. Stand-alone messaging is not supported by A or B. 7. A parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. File Transfer to offline users allowed it set to true. Chat to offline users allowed is set to true. Standalone message enabled is set to false. File Transfer HTTP retention period less than IM S&F period on B side. 8. B parameters: FT MAX SIZE is the same for A, B. Preferred File Transfer technology is HTTP. File Transfer to offline users allowed it set to true. Chat to offline users allowed is set to true. Standalone message enabled is set to false . |
| Test procedure | A selects one file from the local storage and then selects the file transfer option. A selects B and selects to share. Client B is switched online after FT validity period (NNI File Transfer HTTP retention period) but before chat S&F period. B receives the (stored) file download notification and sees an error (file expired). |
| Expected results Post-conditions | 1. RCS capability exchange takes place and A sees that file transfer option is available for the recipient. 2. After becoming online, B receives file transfer download notification stored on MNO B's MSG server and sees the size of the file and an indication of the file type (e.g. MIME icon but no mini-preview). 3. The file is not transferred and received. 4. No display notification is and shown on client A |
| Deep inspection | 1. Verify that capability exchange including HTTP FT tag but without standalone message capability occurs before chat session. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that a new 1-2-1 chat session is created and used to send the FT notification to B 4. In case of support for 1st message in INVITE, verify that FT notification is sent in INVITE. 5. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 6. Verify that chat session is closed afterwards. 7. Verify that the file is invalid due to timeout. 8. Depending on client implementation, verify (a) that no HTTPS requests for file and optional thumbnail are sent to the content server in A's network or (b) an HTTP error is sent back from the content server in A's network. 9. Verify display notification in SIP MESSAGE. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_3_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Unsuccessful HTTP-based file transfer in active one-to-one chat (file size exceeded) |
| Pre-conditions Scenario | 1. A and B are in active 1-2-1 chat session. 2. B has enough free storage space to receive file. 3. The file size being transferred is larger than FT MAX SIZE of MNO B but smaller than the warning file size (FT WARN SIZE) of MNO A. 4. Clients A and B support HTTP-based FT according to former capability exchange. 5. A, B parameters: FT MAX SIZE A is larger than for B. Preferred File Transfer technology is HTTP. Standalone message enabled is set to false. |
| Test procedure | 1. A selects one file from the local storage and then selects the file transfer option. 2. B receives the file download notification and sees an error message due to file size. 3. The file cannot be opened as it is not transferred to B. |
| Expected results Post-conditions | 1. A sees that file transfer is available for the recipient B. 2. B receives file download notification and sees the size of the file and an size error. A file preview may be shown. 3. The file is not transferred and received. 4. No display notification is received and shown on client A. |
| Deep inspection | 1. Verify that capability exchange including FT, HTTP FT tags occurs before chat session. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that FT notification XML is sent inside the active chat. 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5. Depending on client implementation, verify (a) that no HTTPS requests for file and optional thumbnail are sent to the content server in A's network or (b) just an HTTPS request for the optional thumbnail is sent to the content server in A's network and its content is received by client A. Note: It is assumed that the file will always be uploaded successfully. |

| Test Case ID | RCS_6_2_3_5 |
| --- | --- |
| Related test cases |  |
| Tested feature | File Transfer; File Transfer using http |
| Purpose | Delayed HTTP-based file transfer in active one-to-one chat (temp. CS server error or up/download race condition) |
| Pre-conditions Scenario | 1. A and B are in active 1-2-1 chat session. 2. B has enough free storage space to receive file. 3. File size being transferred is smaller than the warning file size (FT WARN SIZE). 4. Clients A and B support HTTP-based FT according to former capability exchange. 5. File download is not possible initially, e.g. because file upload has not been completed but file download notification already sent or the content server in A's network is blocked for some time. 6. A, B parameters: FT MAX SIZE is the same for A, B Preferred File Transfer technology is HTTP |
| Test procedure | 1. A selects one file from the local storage and then selects the file transfer option. 2. B receives and accepts the file download notification if prompted. 3. B opens file. |
| Expected results Post-conditions | 1. A sees that file transfer option is available for the recipient B. 2. B receives file transfer download notification and sees the size of the file and an indication of the file type (e.g. MIME icon). A mini-preview, if available, is only shown after a delay. 3. The file and optional thumbnail are transferred and received after a delay and up to 3 automatic retries. 4. Display notification is received and shown on client A. |
| Deep inspection | 1. Verify that capability exchange including HTTP FT tag occurs before chat session. 2. Verify support of FT HTTP xml content type during SDP negotiation. 3. Verify that FT notification XML is sent inside the active chat 4. Verify that the URL complies to ftcontentserver.rcs.mnc<MNC>.mcc<MCC>.pub.3gppnetwork.org. 5.Verify that an HTTP error is sent back temporally as answer to the HTTPS requests for file and optional thumbnail to the content server in A's network. 6. Depending on the error code sent by the content server verify (a) a retry after RetryAfter header interval out of HTTP 503 or (b) up to 3 retries in case of another HTTP error code. In case of unblocked server successful HTTP 200 responses with content to the last requests shall be received by the client A. 6. Verify display notification in SIP MESSAGE. Note: It is assumed that the file will always be uploaded successfully. |

# Messaging

## Standalone Messaging

### Message Processing

| Test Case ID | RCS_7_1_1_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | Standalone Messaging: Pager Mode |
| Purpose | Send Pager Mode message 1-to-1 |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available |
| Test procedure | A sends a small message (e.g. 100 characters) (Pager Mode Standalone Message) to B with delivery and display notifications requested. |
| Expected results Post-conditions | B receives the message. The message sent by A is shown delivered if successful delivery. How soon the delivery status is available will depend on whether the message is delivered immediately or deferred. |
| Deep inspection | Verify that the message is delivered successfully, either immediately or deferred. The feature tag ‘3gpp-service.ims.icsi.oma.cpm.msg’ for the immediate delivery and ‘3gpp-service.ims.icsi.oma.cpm.deferred’ for the deferred delivery. Verify that the delivery notification is received (SIP MESSAGE). |

| Test Case ID | RCS_7_1_1_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | Standalone Messaging: Pager Mode |
| Purpose | Send Pager Mode message 1-to-Many |
| Pre-conditions Scenario | A, B, and C are RCS Standalone Messaging capable A, B, and C are shown as available |
| Test procedure | A sends a small message (e.g. 100 bytes) (Pager Mode Standalone Message) to B and C with delivery and display notifications requested. |
| Expected results Post-conditions | B and C receive the message. The message sent by A is shown as delivered if successful delivery was received from each recipient. How soon the delivery status is available will depend on whether the message is delivered immediately or deferred. |
| Deep inspection | Verify that the message is delivered successfully to each recipient, either immediately or deferred. The feature tag is ‘3gpp-service.ims.icsi.oma.cpm.msg’ for immediate delivery and ‘3gpp-service.ims.icsi.oma.cpm.deferred’ for the deferred delivery. Verify that the delivery notification is received (SIP MESSAGE) from each recipient. Verify that the recipient list history is sent across NNI (in SIP message body) |

| Test Case ID | RCS_7_1_1_3 |
| --- | --- |
| Related Test Cases |  |
| Feature | Standalone Messaging: Large Message Mode |
| Purpose | Send Large Message Mode message 1-to-1 |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available |
| Test procedure | A sends a image message (Large Message Mode Standalone Message) to B with delivery and display notifications requested B accepts the invitation (either auto or manual) A sends a large text message (e.g. 1500 bytes) to B B accepts the invitation |
| Expected results Post-conditions | B accepts the invitation (either auto or manual acceptance) and receives the image/text message. The multimedia attachment can be rendered and displayed. The message sent by A is shown delivered if successful delivery. How soon the delivery status is available will depend on whether the message is delivered immediately or deferred. |
| Deep inspection | Verify that the invitation is received and accepted Verify that the message is delivered successfully, either immediately or deferred. The feature tag is ‘3gpp-service.ims.icsi.oma.cpm.largemsg’ in SIP INVITE for immediate delivery and ‘3gpp-service.ims.icsi.oma.cpm.deferred’ for the deferred delivery. Verify that the delivery notification is received (MSRP IMDN/CPIM) |

| Test Case ID | RCS_7_1_1_4 |
| --- | --- |
| Related Test Cases |  |
| Feature | Standalone Messaging: Large Message Mode |
| Purpose | Send Large Message Mode message 1-to-Many |
| Pre-conditions Scenario | A, B, and C are RCS Standalone Messaging capable A, B, and C are shown as available |
| Test procedure | A sends a image/large text message (Large Message Mode Standalone Message) to B and C with delivery and display notifications requested. B and C accept the invitation (either auto-accept or manual). |
| Expected results Post-conditions | B and C receive the image/large text message. The multimedia attachment can be rendered and displayed. The message sent by A is shown delivered if successful delivery to all recipients. How soon the delivery status is available will depend on whether the messages are delivered immediately or deferred. |
| Deep inspection | Verify that the invitation is received and accepted by each recipient. Verify that the message is delivered successfully, either immediately or deferred. The feature tag is ‘3gpp-service.ims.icsi.oma.cpm.largemsg’ in SIP INVITE for the immediate delivery and ‘3gpp-service.ims.icsi.oma.cpm.deferred’ for the deferred delivery. Verify that the delivery notification is received (MSRP CPIM) from each recipient. Verify that the recipient list history is sent across NNI (in SIP INVITE) |

### Multi-device Handling

| Test Case ID | RCS_7_1_2_1 |
| --- | --- |
| Related Test Cases | RCS_7_1_1_1 |
| Feature | Standalone Messaging: Pager Mode |
| Purpose | Send Pager Mode message from originating side with multi-device |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available A has 2 devices, A1 and A2, both online/active |
| Test procedure | A1 device sends a small message (e.g. 100 bytes) (Pager Mode Standalone Message) to B with delivery and display notifications requested. |
| Expected results Post-conditions | B receives the message The message sent by A1 is shown delivered if successful delivery. How soon the delivery status is available will depend on whether the message is delivered immediately or deferred. A2 will not receive any delivery notification. A2 will get the delivery message state by message synchronization if Network Message Storage is supported. |
| Deep inspection | Verify that the delivery notification is received (SIP MESSAGE) only on the device that originated the message. |

| Test Case ID | RCS_7_1_2_2 |
| --- | --- |
| Related Test Cases | RCS_7_1_1_1 |
| Feature | Standalone Messaging: Pager Mode |
| Purpose | Send Pager Mode message to a recipient with multiple devices |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available B has 2 devices, B1 and B2, both online/active |
| Test procedure | A sends a small text message (Pager Mode Standalone Message) to B with delivery and display notification request Both B1 and B2 display the message |
| Expected results Post-conditions | Both B1 and B2 receive the message. A will only receive one delivery notification, not multiple delivery notifications. |
| Deep inspection | Verify that the delivery notification is sent by B1 and B2. Verify that the delivery notification is received only once. (i.e., only one delivery notification will be sent across NNI). The duplicate notification is discarded by B’s Messaging Server. |

| Test Case ID | RCS_7_1_2_3 |
| --- | --- |
| Related Test Cases | RCS_7_1_1_3 |
| Feature | Standalone Messaging: Large Message Mode |
| Purpose | Send Large Message Mode message from an originatorwith multi-device |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available A has 2 devices, A1 and A2, both online/active |
| Test procedure | A1 device sends a multimedia message (Large Message Mode Standalone Message) to B with delivery and display notifications requested. B accepts the invitation. |
| Expected results Post-conditions | B receives the message The message sent by A1 is shown delivered if successful delivery. A2 will not receive any delivery notification. A2 will get the delivery message state by message synchronization if Network Message Store is supported. |
| Deep inspection | Verify that the delivery notification is received only on the device that originated the message. |

| Test Case ID | RCS_7_1_2_4 |
| --- | --- |
| Related Test Cases | RCS_7_1_1_3 |
| Feature | Standalone Messaging: Large Message Mode |
| Purpose | Send Large Message Mode message to a recipient with multi-device |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available B has 2 devices, B1 and B2, both online/active |
| Test procedure | A sends a multimedia message (Large Message Mode Standalone Message) to B with delivery and display notifications requested Both B1 and B2 display the message. |
| Expected results Post-conditions | Both B1 and B2 receive the message. A will receive one delivery notification only, not multiple notifications. |
| Deep inspection | Verify that the delivery notification is sent by B1 and B2. Verify that the delivery notification is received only once (i.e., only one delivery notification will be sent across NNI). The duplicate notification is discarded by the B’s Messaging Server. |

### Exception Conditions

| Test Case ID | RCS_7_1_3_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | Standalone Messaging: Large Message Mode |
| Purpose | Maximum large message size exceeded |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available A NNI parameters: Max size of large message = xxx MB B NNI parameters: Max size of large message = yyy MB |
| Test procedure | A sends a multimedia message (Large Message Mode Standalone Message) to B with the message size larger than B can support B’s device sees that the file is too big and answers the INVITE with an error message. NOTE: if Network B’s Messaging Server detects the file is too big and will respond with an error message. . |
| Expected results Post-conditions | B detects that the file to be sent is too big (i.e., a=file-selector value is too big), B answers the INVITE with a 488 “Not Acceptable Here” and warning header set to “133 Size exceeded”, or B’s Messaging Server detects that the file to be sent is too big (i.e., a=file-selector value is too big), B’s Messaging Server answers the INVITE with a 403 “Forbidden” and warning header set to “133 Size exceeded” A does not receive the delivery notification |
| Deep inspection | Verify the a=file-selector attribute in the incoming SIP request Verify the Max size of large message parameter defined in Network B B’s Messaging Server detects that the file to be sent is too big (i.e., a=file-selector value is too big) and responds the INVITE with a 403 “Forbidden” and warning header set to “133 Size exceeded”, or B responds the INVITE with a 488 “Not Acceptable Here” and warning header set to “133 Size exceeded” |

| Test Case ID | RCS_7_1_3_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | Standalone Messaging: Large Message Mode |
| Purpose | Unsupported Media Type |
| Pre-conditions Scenario | A and B are RCS Standalone Messaging capable A and B are shown as available |
| Test procedure | A sends a multimedia message (Large Message Mode Standalone Message) to B with media type which is not supported by B. |
| Expected results Post-conditions | B accepts the INVITE so the session is set up between A and B. B rejects the MSRP SEND request that contains a content-type not supported by B. The session between A and B is torn down. |
| Deep inspection | Verify that the MSRP SEND response is set to 415. |

## 1-to-1 Chat

### Session Management

| Test Case ID | RCS_7_2_1_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user initiates a 1-1 chat with another CPM user |
| Pre-conditions Scenario | A and B are OMA CPM users A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =0 Network B NNI parameters: Message in INVITE =0 |
| Test procedure | A initiates a 1-1 chat with B without typing a message (i.e., no message in SIP INVITE) B is informed of the chat invitation and accepts the invitation (either auto or manual) A or B are ready to chat |
| Expected results Post-conditions | B accepts the invitation (either auto or manual acceptance) Chat session is established and ready for chat |
| Deep inspection | Verify the invitation is received and accepted Verify the chat session is set up |

| Test Case ID | RCS_7_2_1_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat; CPM NNI |
| Purpose | CPM user initiates a 1-1 chat with CPM user with first message in INVITE on originating network – accepted |
| Pre-conditions Scenario | A is a CPM user B is a CPM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A initiates chat with B by typing an initial message1 and then sends it to B B’s device accepts the invitation(either auto or manual) B receives the initial message1 displayed as a chat message |
| Expected results Post-conditions | After B accepts, the chat session is setup B receives Message1 A receives the delivery notification on the initial message(s) , if requested Note: depending how long the acceptance is returned (e.g. network delay) the initial message may be received by B as Pager Mode standalone messages until the SIP INVITE is accepted (see Related Test Cases). |
| Deep inspection | Verify that the invitation is received and accepted Verify that the initial message is in the CPIM wrapper on originating side If the terminating network supports Standalone Messaging and the session is not yet established, the initial message may be sent via Pager Mode Standalone Message. Verify if this is the case and that a delivery notification is sent by B and received by A via SIP MESSAGE. Verify that the chat session is set up and MSRP connection established. If no Standalone Message is sent carrying the initial message, verify that the initial message is received and the delivery notification is sent via MSRP SEND as a chat message. If a standalone message is received, (assuming supported by the receiving network), verify the Pager Mode standalone message is received with the same Conversation ID as the chat session. |

| Test Case ID | RCS_7_2_1_3 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_2 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user initiates a 1-1 chat with CPM user with first message in INVITE on originating network – delayed acceptance |
| Pre-conditions Scenario | A is a CPM user B is a CPM user A and B are RCS Chat capable B is StandaloneMsg capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A initiates chat with B by typing an initial message and then sends it to B B delays the acceptance of the invitation (but will accept later before SIP INVITE times out ) B receives the initial message as a Pager Mode standalone message B accepts the invitation before SIP INVITE times out |
| Expected results Post-conditions | Before B accepts the invitation, B receives the initial message as a Pager Mode standalone message After B accepts, the chat session is setup A receives the delivery notification on the initial message, if requested |
| Deep inspection | Verify that the initial message is in the CPIM wrapper in SIP INVITE from A Verify that the initial message is received by B as a Pager Mode Standalone Message Verify that A receives delivery notification for the initial message Verify that the chat session is set up after B accepts the SIP INVITE |

| Test Case ID | RCS_7_2_1_4 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user initiates a 1-1 chat with CPM user with first message in INVITE on originating network –no answer |
| Pre-conditions Scenario | A is a CPM user B is a CPM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Network B implements manual accept Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A starts chat to B by typing an initial message and then sends it to B B will be informed of the incoming chat invitation. B does not answer |
| Expected results Post-conditions | B receives the initial message as a standalone message, if supported; otherwise, as legacy message A will receive the delivery notification for the initial message which is sent either as a standalone or legacy message ) |
| Deep inspection | Verify that the invitation is received by B but timeout (SIP 408 or 487) Verify the initial message is received as either standalone message or legacy. Verify A receives the delivery notification from B, if requested, for the initial message which is sent either as a standalone or legacy message |

| Test Case ID | RCS_7_2_1_5 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_2 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user initiate a 1-1 chat with CPM user with first message in INVITE on originating network – rejected |
| Pre-conditions Scenario | A is a CPM user B is a CPM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE enabled CPM NNI does not allow first message in INVITE Network B implements manual accept |
| Test procedure | A starts chat to B by typing an initial message and then sends it to B B will be informed of the incoming chat invitation B rejects the invitation |
| Expected results Post-conditions | There is no chat session setup up between A and B B does not receive the initial message |
| Deep inspection | Verify that B rejects the invitation with 603, which is propagated back to A |

| Test Case ID | RCS_7_2_1_6 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat: SIMPLE IM NNI |
| Purpose | SIMPLE IM user initiate a 1-1 chat with SIMPLE IM user with first message in INVITE - accepted |
| Pre-conditions Scenario | A is a SIMPLE IM user B is a SIMPLE IM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Network B NNI parameters: Message in INVITE =1 Network A and Network B use Message Server |
| Test procedure | A starts chat to B by typing an initial message and then sends it to B B gets the message (notification bar) and accepts the INVITE by responding to the message B sends the delivery notification for the initial message, if requested |
| Expected results Post-conditions | B gets the initial message (notification bar) When B starts to responds to the message, the chat session is setup A receives the delivery notification to those initial messages sent before the chat session is setup |
| Deep inspection | Verify that the invitation is received Verify that the initial message is received Verify that A receives the delivery notification from B, if requested. |

| Test Case ID | RCS_7_2_1_7 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_6 |
| Feature | 1-1 Chat: SIMPLE IM NNI |
| Purpose | (IM-IM) SIMPLE IM initiate a 1-1 chat with SIMPLE IM user with first message in INVITE – no answer |
| Pre-conditions Scenario | A is a SIMPLE IM user B is a SIMPLE IM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Network B NNI parameters: Message in INVITE =1 Network A and Network B use Message Server |
| Test procedure | A starts chat to B by typing an initial message and sends it to B B gets the message, but does not respond A sends multiple messages (in multiple INVITE) with no response After some time, all the INVITE requests expire, including the last INVITE |
| Expected results Post-conditions | B sees the message from A in the notification bar but does not open the chat or respond to the message Chat session is not set up between A and B After the INVITE timeout, the INVITE is cancelled/terminated by Message server A receives the delivery notifications for those messages in INVITE requests |
| Deep inspection | Verify the initial messages are delivered via successful invitations Verify that the last invitation is cancelled(487) after invitation timeout (408), and Messaging Server maps the 408/487 into 486 before propagating it to the sender. Verify that the B client responds with 486 for each earlier INVITE when a new INVITE arrives. Verify delivery notifications to the initial message is received by A in SIP MESSAGE |

| Test Case ID | RCS_7_2_1_8 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | Simple IM initiates a 1-1 chat with CPM user with first message in INVITE - accepted |
| Pre-conditions Scenario | A is SIMPLE IM user B is CPM Chat user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 The interworking function implements a timer to wait for the session is setup for sending the initial message Note: CPM NNI does not allow first message in INVITE |
|  | A starts chat to B by typing an initial message and then sends it to B B is informed of the chat invitation. B accepts the invitation (either auto or manual), B will receive the initial message displayed as chat message Note: depending how long the response is received from receiving network or the implementation of the interworking function, the initial and subsequent messages may be received by B as Pager Mode standalone message until the SIP INVITE is accepted. |
| Expected results Post-conditions | Until the SIP INVITE response from B is received, some of the initial messages may be received as Pager Mode standalone message(s) After B accepts, the chat session is setup between A and B A receives the delivery notification on the initial message(s) , if requested |
| Deep inspection | Verify the invitation is received with the header mapping according to RCS NNI Interworking Guideline IR.90 section 6.3.1 Verify the initial message is received from the CPIM wrapper on originating side (i.e., from IM user) Verify the chat session is set up and MSRP connection established so the initial message is received and the delivery notification is sent in MSRP SEND Verify Pager Mode standalone message is received if so implemented by interworking function |

| Test Case ID | RCS_7_2_1_9 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_8 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | ) SIMPLE IM user initiates a 1-1 chat with CPM user with first message in INVITE on originating network - no answer |
| Pre-conditions Scenario | A is SIMPLE IM user B is CPM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Network B implements manual accept Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A starts chat to B by typing an initial message and then sends it to B B will be informed of the chat invitation B does not answer |
| Expected results Post-conditions | B receives the initial message as standalone message, if supported; otherwise, as legacy message No chat session is setup between A and B A receives the delivery notification for the initial message which is sent as either a standalone or legacy message) |
| Deep inspection | When the invite is timeout(SIP 408), verify the initial message is received as either standalone message or legacy. Verify no chat session is setup Verify A receives the delivery notification from B, if requested. |

| Test Case ID | RCS_7_2_1_10 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_8 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | SIMPLE IM user initiates a 1-1 chat with CPM user with first message in INVITE on originating network – rejected |
| Pre-conditions Scenario | A is SIMPLE IM user B is CPM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Message in INVITE =1 Network B implements manual accept Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A starts chat to B by typing an initial message and then sends it to B B is informed of the chat invitation. B rejects the invitation |
| Expected results Post-conditions | B does not receive the initial message in the INVITE No chat session is setup between A and B A does not receive the delivery notification for the initial message |
| Deep inspection | When the invite is rejected (SIP 603), verify that the initial message is not delivered to B Verify no chat session is setup Verify A does not receives the delivery notification from B |

| Test Case ID | RCS_7_2_1_11 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | (CPM-IM) CPM user initiate a 1-1 chat with SIMPLE IM user – success |
| Pre-conditions Scenario | A is CPM user B is SIMPLE IM user A and B are RCS Chat capable A and B are shown as available5. Network B NNI parameters: Message in INVITE =1 6. Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A starts chat to B A types the message1 B receives the initial message displayed as a chat message B responds to the message2 Session is setup between A and B |
| Expected results Post-conditions | B gets the initial message (on notification bar) and receives the chat message1 from A A receives the delivery notification on message1 , if requested When B responds to the message1, the chat session is setup A receives the delivery notification on message2, if requested |
| Deep inspection | Verify the MSRP session is setup on the A leg and messages sent by A is stored and copied to CPIM body in SIP INVITE request to B Verify that the SIP INVITE is received by B with a=accept-wrapped-types:text/plain Verify that the first message is included as the CPIM body in the SIP INVITE to B Verify the delivery notification is received by A in SIP MESSAGE for the first message1 and in MSRP SEND for message2 |

| Test Case ID | RCS_7_2_1_12 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_11 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | (CPM-IM) CPM user initiates a 1-1 chat with SIMPLE IM user – no response or error response |
| Pre-conditions Scenario | A is CPM user B is SIMPLE IM user A and B are RCS Chat capable A and B are shown as available initially Network B NNI parameters: Message in INVITE =1 Network B implement manual accept Note: CPM NNI does not allow first message in INVITE |
| Test procedure | A initiates chat with B A types a text message1 Message1 is displayed on B device (e.g. notification bar) No response is received from B (e.g., B is away from device) Session is not setup between A and B yet A types more messages message2 and message3 BMessage2 and message3 are displayed on B device B still does not respond Session is still not setup between A and B yet A few minutes later, B responds and chat session setup A sends message4 B receives message4 |
| Expected results Post-conditions | B receives the chat message1, message2 , and message3 (i.e., message displayed on chat window) but does not respond (e.g. ignore, away from device) Later, B accepts one invitation by responding to the message and a chat session is set up B receives messge4 A receives a delivery notification, if requested, for each chat message that was delivered to B’s device |
| Deep inspection | Verify that multiple SIP INVITE requests are received by B; one per each message sent by A until B responds to the INVITE (for this case, 3 SIP INVITE requests for 3 messages sent by A) Verify that the latest session is used. That is, there is no multiple chat session with the same user at any time. B will send SIP BYE to cancel the previous session and accept the new INVITE to establish the new session. Verify the delivery/display notifications for message1, message2, and message3 in SIP INVITE are sent using SIP MESSAGE by B and for message4 in MSRP SEND. |

| Test Case ID | RCS_7_2_1_13 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | 1-1 chat session timeout and restart |
| Pre-conditions Scenario | A is a either CPM or SIMPLE IM user B is a either CPM or SIMPLE IM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameter: 1-to-1 IM session inactivity timer = xxx sec Network B NNI parameter: 1-to-1 IM session inactivity timer = yyy sec The 1-1 chat session is active |
| Test procedure | A is idle more than its 1-to-1 IM session inactivity timer A starts responding to a chat with B in the conversation and sends to B B accepts the invitation and receives the message according the behaviour of IM or CPM user. |
| Expected results Post-conditions | After no activity longer than A’s IM session inactivity timer parameter, A starts chat which result in a new chat setup The chat session is started B receives messages |
| Deep inspection | Verify that the session is timeout with SIP BYE received by A and B Verify that the chat session is restarted with SIP INVITE when one of the users starts chat. |

### Message Handling

| Test Case ID | RCS_7_2_2_1 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_1 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user sends chat message to CPM user |
| Pre-conditions Scenario | A is CPM user B is CPM user A and B are RCS Chat capable A and B are shown as available 1-1 Chat session between A and B is active Network A and Network B support multimedia contents in chat |
| Test procedure | A sends a multimedia content, either from gallery or camera B receives the multimedia message A sends a text message B receives messages and click on the multimedia content, the message is displayed/played |
| Expected results Post-conditions | When A is composing, B receives an indication of A typing B receives the messages A receives the delivery notifications, if requested |
| Deep inspection | Verify that IsComposing notification is displayed while one side is typing Verify that the message is received by B Verify A receives the delivery notification from B, if requested Verify A receives the display notification from B, if enabled by B |

| Test Case ID | RCS_7_2_2_2 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_6 |
| Feature | 1-1 Chat: IM NNI |
| Purpose | IM user sends chat message to IM user |
| Pre-conditions Scenario | A is SIMPLE IM user B is SIMPLE IM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Multimedia in chat enabled is disabled Network B NNI parameters: Multimedia in chat enabled is disabled 1-1 Chat session between A and B is active |
| Test procedure | A types a text message and sends it to B B receives the message B responds to the message |
| Expected results Post-conditions | A is typing. B receives an indication of A typing. A sends the message. B will receive the message (notification bar) and read the message (open chat window) A will receive the delivery notification and display notification, if enabled by B A will receive the message from B B will receive the delivery notification and display notification, if enabled by A |
| Deep inspection | Verify that IsComposing notification is displayed while one side is typing Verify that the message is received by B Verify A receives the delivery notification from B, if requested Verify A receives the display notification from B, if enabled by B |

| Test Case ID | RCS_7_2_2_3 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_8 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user sends chat messages |
| Pre-conditions Scenario | A is CPM user B is SIMPLE IM user A and B are RCS Chat capable A and B are shown as available Network A NNI parameters: Multimedia in chat enabled is enabled Network B NNI parameters: Multimedia in chat enabled is disabled Network A and Network B use Message Servers The 1-1 Chat session is active |
| Test procedure | A sends a text message1 B receives the text message1 and responds with a text message2 A sends a multimedia content message3 |
| Expected results Post-conditions | B receives the text message1 B will receive the multimedia message3 as a Large Message Mode Standalone Message or as a File Transfer A will receive delivery notification for the multimedia message3, if it is sent as a Large Message Mode Standalone Message. A will not receive delivery notification if it is sent as a File Transfer. |
| Deep inspection | Verify that when B responds to the chat invitation, the a=accept-wrapped-types attribute did not contain any multimedia types. This will make it clear to A that to send a multimedia message it has to be sent in a separate session as a Large Message Mode Standalone Message or as a File Transfer depending on local implementation Verify that the delivery notification is received by A for the text message1 Verify that the delivery notification is received by A for the multimedia message, if it is sent as a Large Message Mode Standalone Message. A will not receive delivery notification if it is sent as a File Transfer. |

| Test Case ID | RCS_7_2_2_4 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat |
| Purpose | Verify disposition notifications sent when chat session is over |
| Pre-conditions Scenario | A and B are either CPM or SIMPLE IM users A and B are RCS Chat capable A and B are shown as available 1-1 Chat session between A and B is active |
| Test procedure | A types a message1 and sends the message B receives message1 and reads message1 B is then away from the device A sends additional message2 B receives message2 but does notread message2 A and B are idle for some period time and the session is timeout B returns to the device and reads the message2 |
| Expected results Post-conditions | When A is composing, B receives an indication that A is typing. When B reads messge1, A receives the delivery notification and display notification for message1 A receives the delivery notification for message2 At a later time, when B reads message2, A receives the display notification for message2 |
| Deep inspection | Verify that IsComposing notification is displayed while one side is typing Verify that delivery and display notification for message1 is carried in CPIM/IMDN in MSRP SEND Verify the display notification for message2 is in SIP MESSAGE ( because session is over) |

### Multi-device Handling

| Test Case ID | RCS_7_2_3_1 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_1, RCS_7_2_1_2 |
| Feature | 1-1 Chat: CPM NNI |
| Purpose | CPM user initiates a 1-1 chat with multi-device user |
| Pre-conditions Scenario | A is a CPM user B is a CPM user A and B are RCS chat capable A and B are shown as available B has 2 devices, B1 and B2, both online/active Network A and Network B use Messaging Server Optionally, Network-based Common Message Store is available in Network B |
| Test procedure | A initiates a chat with B User devices B1 and B2 receive the invitation User device B2 accepts the invitation A sends message1 B2 receives message1 A sends additional messages: message2 and message3 B2 receives all messages If Network-based Common Message Store is available in Network B, proceed with the following steps B1 displays all messages and the message state B1 sends message4 A accepts the invitation. The chat session between A and B1 is set up A sends a message5 B1 receives the message5 B2 displays message4 and message5 |
| Expected results Post-conditions | The chat session is set up between A and B2 when B2 accepts the invitation The chat session towards B1 is terminated A receives the delivery notification for all messages sent The chat session is setup between A and B1 when B1 sends message4 A terminates the session between A and B2 A receives message4 B1 receives the delivery notification for message4 from A B1 receives message5 A receives delivery notification for message5 from B1 |
| Deep inspection | Verify that both B1 and B2 receive SIP INVITE from A Verify that the session towards B1 is terminated with SIP BYE from the Messaging server Verify that the delivery notification is received from B2 only. No multiple disposition notifications should be received or sent across NNI. B’s Messaging server will discard the duplicate delivery notification Verify that the session between A and B1 is active when B1 responds to message3 with message4 and session between A and B2 is terminated |

| Test Case ID | RCS_7_2_3_2 |
| --- | --- |
| Related Test Cases | RCS_7_2_1_6 |
| Feature | 1-1 Chat: IM NNI |
| Purpose | IM user with multi-device Initiate 1-1 chat with IM user |
| Pre-conditions Scenario | A is a SIMPLE IM user B is a SIMPLE IM user A and B are RCS chat capable A and B are shown as available A has 2 devices, A1 and A2, both online/active Network A and Network B use Messaging server |
| Test procedure | Device A1 initiates a chat with B Device A1 sends message1 B receives message1 A1 sends additional message2 B receives all messages |
| Expected results Post-conditions | The chat session is setup between A1 and B A1 receives the delivery notifications for all messages |
| Deep inspection | Verify that the delivery notification is received on A1 only |

### Exception Conditions

| Test Case ID | RCS_7_2_4_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | 1-1 Chat |
| Purpose | Chat message size limit |
| Pre-conditions Scenario | A and B are RCS chat capable A and B are shown as available Network A and Network B use Messaging Server Network A NNI Parameters Max size of 1-to-1 message = xx MB Network B NNI Parameters Max size of 1-to-1 message = yy MB Chat session is active |
| Test procedure | A sends a message with size larger than what B can support |
| Expected results Post-conditions | The Messaging Server B will not forward the message to B B does not receive the message A does not receive the delivery notification from user B |
| Deep inspection | Verify that B network detects the message is too large during transmitting (MSRP SEND). The message is not delivered to B. Verify that A receives MSRP failure REPORT and will not receive delivery notification from B. |

## Group Chat

### Session Management

| Test Case ID | RCS_7_3_1_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Initiate a group chat with dynamic focus |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A, B, and C are RCS Chat capable A, B, and C are shown as available Network A NNI parameters: Auto-accept of group chat enabled Chat enabled and group chat enabled Group Chat focus allows restarts disabled (dynamic focus) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Chat enabled and group chat enabled Network C NNI Parameters: Auto-accept of group chat enabled Chat enabled and group chat enabled |
| Test procedure | A initiates group chat with B and C with a Group Chat Test Case ID A B receive the invitation and accepts the invitation Session setup with A and B A sends a message1 C receives and accepts the invitation B receives message1 C receives message1 A receives delivery notification from B and C A may receive display notification from B or C |
| Expected results Post-conditions | B receives and accepts the invitation Group session established with participant list: A(connected), B(connected), and C(pending) C receives and accepts the invitation. A and B get the notification of C having joined the conversation Note if B and C accept the invitation at close to the same time, thegroup chat will be set up with A, B, and C from very beginning and there would be no new notification event package B and C receive message1 A receives the delivery notification from B and C for message1 |
| Deep inspection | Verify that the conference state is sent when C joins Verify that the group chat session is set up |

| Test Case ID | RCS_7_3_1_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Initiate a group chat with static focus |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user A , B, and C are RCS Chat capable A , B, and C are shown as available Network A NNI parameters: Auto-accept of group chat enabled b. Chat enabled and group chat enabled Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled (static focus) |
| Test procedure | C initiates group chat with A and B with a Group Chat Test Case ID C A and B receive the invitation and accepts the invitation Session setup with A and B C sends a message1 A receives message1 B receives message1 C receives delivery notification from A and B C may receive display notification from A and B |
| Expected results Post-conditions | Group session is established with participant list A, B, and C When C send message1, A and B receive message1 C receives the delivery notification from A and B for message1 |
| Deep inspection | Verify that the invitation is received by A and B with the header mapping according to RCS NNI Interworking Guideline IR.90 section 6.3.1 Verify that C receives the disposition notification for message1 from A and B |

| Test Case ID | RCS_7_3_1_3 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Initiate a closed group chat |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A , B, and C are RCS Chat capable A , B, and C are shown as available Network A NNI parameters: Auto-accept of group chat enabled Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled |
| Test procedure | B initiates a closed group chat with A and C with a Group Chat Test Case ID B A receives the invitation and accepts the invitation C receives the invitation and accepts the invitation A closed group session is setup among A, B, C B sends a message1 |
| Expected results Post-conditions | The session invitation indicates the participants A, B, and C When A accepts the invitation, the group session is established with A and C participants When B accepts the invitation, A and C will get indication “ B has joined the conversation” with the conference state (Note: If A and B accept the invitation near the same time, then the group session will be setup with A,B, and C from very beginning. ) A receives message1 C receives message1 B receives delivery notification from A and C B may receive display notification from A or C |
| Deep inspection | Verify that the attribute in the SDP of SIP INVITE contains the SDP attribute a=chatroom with OMA CPM 2.0 private token for closed group chat. |

| Test Case ID | RCS_7_3_1_4 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Group session timeout with dynamic focus |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user A , B, and C are RCS Chat capable A , B, and C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The group session is active and Network A is the conference focus with Group Chat Test Case ID A |
| Test procedure | B send message1 A and C receive messge1 No activity for more than A’s Group IM session inactivity timer and session timeout Session is torn down |
| Expected results Post-conditions | It is transparent to end user A, B, C when the session is terminated due to timeout and the session has been torn down |
| Deep inspection | Verify the focus server will terminate the subscription of all participants Verify the SIP BYE 480 sent by focus server Chas a Reason header , e.g. SIP;cause=480;text=”Bearer unavailable” Note: the Session Identity is not kept (Service Provider dependent) on focus server Note: the latest participant list is not kept on the focus server |

| Test Case ID | RCS_7_3_1_5 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Group session timeout with static focus |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A , B, and C are RCS Chat capable A , B, and C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The group session is active and Network C is the conference focus with Group Chat Test Case ID C |
| Test procedure | B send message1 A and C receive messge1 No activity for more than C’s Group IM session inactivity timer and session timeout Session torn down |
| Expected results Post-conditions | It is transparent to end user A, B, C when the session is terminated due to timeout and session has been torn down |
| Deep inspection | Verify the focus server will terminate the subscription of all participants Verify the SIP BYE 480 sent by focus server Chas a Reason header , e.g. SIP;cause=480;text=”Bearer unavailable” Note: the Session Identity is kept (Service Provider dependent) on focus server Note: the latest participant list is kept on the focus server |

| Test Case ID | RCS_7_3_1_6 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Restart group session with dynamic focus |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A , B, and C are RCS Chat capable A , B, and C are shown as available Network A NNI parameters: Auto-accept of group chat enabled Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The group session hosted by Network A with Group Chat Test Case ID A is not active (inactivity timeout); The last participant list has A, B, C |
| Test procedure | C reply to message1 on a conversation which has been idle for some time C type message2 and send it A and B receives invitation from focus server C with the previous Group Chat Test Case ID A A and B accept the invitation Group session restarted with focus server C |
| Expected results Post-conditions | It is transparent to end user A, B, C when the session is restarted A and B receive message2 C receives delivery notification from A and B |
| Deep inspection | Verify that the rejoin INVITE from C with Session Identity A will fail with 404 Verify C initiates a new group session with the same Group Chat Test Case ID A and new Session Identity C using the last participant list from the last conference event package notification |

| Test Case ID | RCS_7_3_1_7 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Restart group session with static focus |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A , B, and C are RCS Chat capable A , B, and C are shown as available Network A NNI parameters: Auto-accept of group chat enabled Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The group session hosted by Network C with Group Chat Test Case ID C is not active (inactivity timeout); the last participant list has A, B, C |
| Test procedure | A type message2 on a conversation (hosted by focus server C ) B and C receives invitation from focus server C with the previous Group Chat Test Case ID C B and C accept the invitation Group session restarted (with the same focus server C) |
| Expected results Post-conditions | It is transparent to end user A, B, C when the session is restarted B and C receive message2 (session restarted) A receive delivery notification |
| Deep inspection | Verify the rejoin INVITE from A with Session Identity C will invoke focus server C to initiate a group session with the last participant list A, B, C kept by Focus server C Verify C initiates the group session with the same Group Chat Test Case ID C using the last participant list stored when the session was timeout due to inactivity |

| Test Case ID | RCS_7_3_1_8 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Restart a closed group session |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A, B, and C are RCS Chat capable A, B, and C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The closed group session is idle and Network B is the conference focus with Group Chat Test Case ID B A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable |
| Test procedure | A types message3 on a idle chat where B and C are on the participant list (hosted by B) B sends message4 |
| Expected results Post-conditions | B and C receives session invitation (for a closed group chat) and accept it B and C receives message3 A receives delivery notification from B and C A and C receives message4 B receives delivery notification from A and C |
| Deep inspection | Verify that the restart INVITE from A with Session Identity B fails with 404 (due to dynamic focus) Verify that the attribute a=chatroom with private token for CPM 2.0 closed group chat in the SDP of SIP INVITE request from A |

| Test Case ID | RCS_7_3_1_9 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Add new participant to a closed group chat |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A, B, and C are RCS Chat capable A, B, and C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The closed group session is idle and Network B is the conference focus with Group Chat Test Case ID B A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable |
| Test procedure | A add D to the chat |
| Expected results Post-conditions | Adding D is denied (UI dependent: may get warning message s “ No new participant can be added to a closed group chat”) |
| Deep inspection | Verify that A receives a SIP 403 “Forbidden” response with Warning header text set to “127 Service not authorised” |

| Test Case ID | RCS_7_3_1_10 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Restart group session from full store and forward participant |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user with A, B, and C are RCS Chat capable A, B, and C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) The group session is not active and Network A is the conference focus with Group Chat Test Case ID A A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable |
| Test procedure | B type message3 on a idle conversation where A and C are on the participant list (hosted by A) |
| Expected results Post-conditions | A receives a session invitation (for a Large Message Mode message ) and accept it A receives message3 C receive message3 as legacy (SMS/MMS) message No group chat session is setup B receive delivery notification from A and C Note: the implementation is Service Provider dependent. The use case above is one option. |
| Deep inspection | Verify the rejoin INVITE from B with Session Identity A will fail with 404 Verify a Large Message Mode session invitation is initiated to A but not to C Verify legacy message is sent either via SMS/MMS Interworking or from device client directly based on capability. |

| Test Case ID | RCS_7_3_1_11 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Restart group session with one user offline or no answer |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user A, B, C are RCS Chat capable A, B, C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable The group chat hosted by C is active |
| Test procedure | A , B, C are in chat session and then stop exchange message for a while. B becomes offline. Then the group session timeout. C sends message1 and starts exchanging messages A receives invite and accept it B is still offline A gets the message1 B becomes online and rejoin the group chat session A and C get indication on B having joined A sends message2 B and C get the message2 |
| Expected results Post-conditions | When C sends message1, the group session restarts with A, B, and C. The invite to B times out and A accepts the invite When B becomes online, B is able to re-join the group chat because of static focus A and C are informed of B having joined When C sends message2, both A and B get the message2 |
| Deep inspection | Verify that the invite is sent to B and C using previous Group Chat Test Case ID. Verify that B sends re-join INVITE to the same session identity of C |

| Test Case ID | RCS_7_3_1_12 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Extend 1-1 chat to group chat |
| Pre-conditions Scenario | A is a CPM user B is a CPM user C is a SIMPLE IM user or CPM user A, B, and C are RCS Chat capable A, B, and C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) Multimedia in chat enabled is disabled A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable The 1-1 chat session between A and C is active |
| Test procedure | A and C are in ongoing chat session A add B to the chat B receives the invite and accepts it C also receives the invite and accept it C sends text message1 Both A and B gets message1 B sends message2 and both A and C get message2 |
| Expected results Post-conditions | When the new group chat is created, C receives the group chat invite. C may get an indication that the group chat is a replacement for the 1-1 chat between A and C C accepts it, and tears down the 1-1 chat between A and C. B receives the group chat invite B accepts it When C sends text message1, both A and B get the message1 When B sends text message2, both A and C get the message2 |
| Deep inspection | Verify SIP REFER with 202 response to add B and C to the new group chat Verify IsComposing and disposition notifications Verify that the SIP INVITE to C has the Session-Replaces header so C may indicate to user C that this is a replacement for the 1-1 chat Verify that C subscribes to the conference state event package to get the participant to display the participant list to user C Verify that B subscribes to the conference state event package to get the participant to display the participant list to user B |

| Test Case ID | RCS_7_3_1_13 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Leaving a group chat |
| Pre-conditions Scenario | A is an CPM user B is an CPM user C is a SIMPLE IM user A, B, C are RCS Chat capable A, B, C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Multimedia in chat enabled is disabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable The regular group chat hosted by C is active |
| Test procedure | A leaves the group chat explicitely |
| Expected results Post-conditions | B and C get notification that A has left |
| Deep inspection | Verify that A sends SIP BYE to Conference focus server C Verify that conference state event package notification is sent to B and C Verify that Conference focus server C removes A from the participant list |

| Test Case ID | RCS_7_3_1_14 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | User rejoins an inactive group session that the user has left voluntarily |
| Pre-conditions Scenario | A is an CPM user B is an CPM user C is a SIMPLE IM user A, B, C are RCS Chat capable A, B, C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Network B NNI parameters: Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Multimedia in chat enabled is disabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable A has left explicitly the group chat hosted by C previously The regular group chat hosted by C is not active |
| Test procedure | A tries to rejoin by responding a message to the group chat hosted by C that A left voluntarily |
| Expected results Post-conditions | The rejoin fails due to authorization |
| Deep inspection | Verify that the Session Identity C and Group Chat ID C are included in the rejoin INVITE from A and the rejoin fails with 403 Verify the rejoin from A who has left explicitly will fail with 404 while the group chat hosted by C is inactive |

| Test Case ID | RCS_7_3_1_15 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Rejoin to an active regular group chat that the user has left previously |
| Pre-conditions Scenario | A is an CPM user B is an CPM user C is a SIMPLE IM user A, B, C are RCS Chat capable A, B, C are shown as available Network A NNI parameters: Group IM session inactivity timer=xxx sec (e.g., 300) Network B NNI parameters: Auto-accept of group chat enabled Group chat full store and forward enabled Group chat Invite only full store forward enabled Group IM session inactivity timer=yyy sec (e.g., 300) Network C NNI Parameters: Auto-accept of group chat enabled Multimedia in chat enabled is disabled Group Chat focus allows restarts enabled Group IM session inactivity timer=zzz sec (e.g., 300) A is StandaloneMsg capable B is StandaloneMsg capable C is not StandaloneMsg capable A has left group chat hosted by C The regular group chat hosted by C is active with participants B and C |
| Test procedure | A tried to rejoin the group chat session with the Session Identity C which A left previously by responding to a chat message from the group chat B adds A to the group chat hosted by C C is notified that A has joined C sends message1 |
| Expected results Post-conditions | When A rejoin, the rejoin fails with SIP 403 “Forbidden” response and a Warning warning text set to “122 Function not allowed” in the response When B adds A, A joins the active group chat hosted by C successfully B and C are notified of A having joined and listed in the participant list When C sends message1, A and B receive message1 |
| Deep inspection | Verify that when A tries to rejoin the chat group, SIP 403 “Forbidden” response and a Warning header with the warning text set to “122 Function not allowed” are returned. Verify that when B adds A, the SIP REFER with 202 response is returned |

### Message Handling

### Multi-device Handling

The test case for Multi-device handling for group chat is the same as the one for  1-1 chat.

### Exception Conditions

| Test Case ID | RCS_7_3_4_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Maximum size of IM content limit |
| Pre-conditions Scenario | A, B, C are RCS chat capable A, B, C are shown as available Network A, Network B, and Network C use Messaging Server Chat session is active Network A NNI parameters: Maximum size of IM content = xx MB Network B NNI parameters: Maximum size of IM content = yy MB Network C NNI Parameters: Maximum size of IM content = zz MB The group session hosted by Network A is active |
| Test procedure | C sends a message which is larger than what B can support |
| Expected results Post-conditions | A receives the message B does not receive the message C receives delivery notification from A but does not receive the delivery notification from B |
| Deep inspection | If Conference Server A receives the “max-size” attribute of SDP from B, Conference server A will not forward the message to B. Note: If Conference Server A does not receive the “max-size” attribute of SDP from B, it sends the message to B Network. B’s Messaging Server detects (from the total size of the message in the Byte-Range parameter of MSRP SEND) the message exceeds their “Maximum size of IM content”, it will not forward the message to B. Verify that C does not receive the delivery notification from B. |

| Test Case ID | RCS_7_3_4_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | Group Chat |
| Purpose | Maximum number of participants in group chat |
| Pre-conditions Scenario | A, B, C are RCS chat capable A, B, C are shown as available Network A, Network B, and Network C use Messaging Server Network A NNI parameters: Max number of participants in group chat session = xx Network B NNI parameters: Max number of participants in group chat session = yy Network C NNI Parameters: Max number of participants in group chat session = zz The group session hosted by Network A is active |
| Test procedure | C adds a new participant that will make the participants to exceed A’s “Max number of participants in group chat session” |
| Expected results Post-conditions | The adding of a participant fails. No new participant is added. C may get error message on UI (UI dependent) |
| Deep inspection | Verify that the maximum number of participants allowed and the current user count for the running group chat is notified by the focus in the maximum-user-count and user-count elements If the maximum-user-count and user-count elements for the running group chat is notified by the focus in or it is provided in the notification event package but is not honoured by C, C will receive a SIP 486 “Busy Here” response and Warning headerwith the warning text set to “102 Too many participants”. |

# Content Sharing

## Video Share

### Basic Video Share

| Test case ID | RCS_8_1_1_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | A shares video with B |
| Pre-conditions Scenario | 2) A and B are in an active voice call 3) Capabilities exchange has taken place confirming Video Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | A starts Video Share to B. B accepts the invite. A sends live video to B. |
| Expected results Post-conditions | B receives the video. |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) If a video session, verify H.264 support in SDP negotiation |

| Test case ID | RCS_8_1_1_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Video Share: Successful simultaneous invites |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible 3) Both handsets support simultaneous Video Share 4) Both devices have front or rear facing camera |
| Test procedure | A and thereafter B send Video Share invites. The procedure is then repeated in opposite order. |
| Expected results Post-conditions | Two Video Share sessions are established (A->B and B->A) |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (both sessions) 2) Verify graceful establishment of the Video Share session (media) via traces (both sessions) 3) Verify H.264 support in SDP negotiation 4) Capability exchange |

| Test case ID | RCS_8_1_1_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Simultaneous Video and Image Share sessions |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2)There is an active Video Share session from A to B 3) Handsets support simultaneous Video/Image Share sessions (one per direction) 4) Both devices have front or rear facing camera |
| Test procedure | A is sharing video with B. Then B decides to share a picture with A. The procedure is then repeated in opposite order. |
| Expected results Post-conditions | The Image Share transference is completed. A can see the image B sent while B can see the video that A sent. Each share session is independent and should be handled separately. |
| Deep inspection | 1) Verify graceful establishment of the Image Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Image Share session (media) via traces (active session) 3) Verify graceful completion of Image Share session and signalling/media release 4) Verify options exchange |

| Test case ID | RCS_8_1_1_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Resilience to several share sessions start and completion |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | A is able to share several items (start and finish a Video Share, then share an image and finally another image) one after the another during the same call with B. |
| Expected results Post-conditions | The Video/Image Share are performed according to specification. |
| Deep inspection | 1) Verify graceful initiation/termination of the different sessions (signalling) via traces 2) Verify graceful handling of media during the sessions via traces |

| Test case ID | RCS_8_1_1_5 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | MSISDN normalization (on outgoing call) provided by network |
| Pre-conditions Scenario |  |
| Test procedure | a) A establishes a voice call to B using local format of B-number |
| Expected results Post-conditions | B’s client receives call invitation with number in international format (E.164) The outgoing voice call from A to B is successfully established |
| Deep inspection | 1) Verify MSISDNs formats in outgoing requests, including tel-uri with phone-context=domain |

| Test case ID | RCS_8_1_1_6 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Identification of the number against the local phone book |
| Pre-conditions Scenario | 1) Only the local format for the number of B is known (e.g. prefix 0) |
| Test procedure | a) B establish a voice call to A b) A’s client receives call invitation with number in international format c) Inspection of the phone book is done and the B contact is successfully identified |
| Expected results Post-conditions | The incoming voice call from B to A is successfully established |
| Deep inspection | 1) Verify MSISDNs formats in incoming requests and responses, including sip-uri with user=phone and phone-context=domain, or tel-uri with phone-context=domain |

### Multiparty call and Video Share

| Test case ID | RCS_8_1_2_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Multiparty. Users were in a CS call without using the image or Video Share services. |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | 1. A establishes a Video Share session with B 2. A establishes a multiparty call with B and C 3. C leaves the call so the call becomes a standard call between A and B |
| Expected results Post-conditions | 1. Voice call established between A and B. 2a. Multiparty call is established among A, B and C 2b. Video sharing between A and B ends 2c. RCS capabilities are updated for A3a. Multiparty call has ended 3b. Both Image and Video Share capabilities are shown as available |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Video Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify session termination (sip/media) 5) Verify capability exchange following multiparty call establishment 6) Verify capability exchange following multiparty call release |

### Call on hold and Video Share

| Test case ID | RCS_8_1_3_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Call on hold. Users were in a CS call using Video Share. |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | 1. A establishes a voice call with B 2. A invites B to share live video 3. B accepts Video Share 4. A puts B voice call on hold 5. A retrieves B’s voice call |
| Expected results Post-conditions | 1. Voice call established between A and B. 2-3. Video sharing starts 4a. Voice call on hold 4b. Video sharing between A and B ends 4c. RCS capabilities are updated for A: image and Video Share services are no longer available 5a. Voice connection is re-established 5b. Video Share is re-established |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Video Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify session termination (sip/media) 5) Verify capability exchange following call on hold action does NOT take place 6) Verify re-establishment of Video Share session |

| Test case ID | RCS_8_1_3_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Call on hold. A performs video sharing with C, after call hold with B |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible |
| Test procedure | 1. A establishes a voice call with B 2. A invites B to share a stored video 3. B accepts video sharing 4. A puts B’s call on hold 5. A establishes a voice call with C 6. A invites C to share a stored video 7. C accepts video sharing |
| Expected results Post-conditions | 1. Voice call established between A and B. 2-3. Video sharing starts A and B 4a. Voice call on hold 4b. Picture sharing between A and B ends 4c. RCS capabilities are updated for A: image and Video Share services are no longer available 5. Voice call established between A and C. 6-7. Video sharing starts between A and C |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Video Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify session termination (sip/media) 5) Verify capability exchange following call on hold establishment (with B) does not take place but it does with C (call become active 6) Verify 1-4 for new session |

| Test case ID | RCS_8_1_3_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Call on hold. Retrieve call on hold + initiate Video Share |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible |
| Test procedure | 1. A establishes a voice call with B 2. A invites B to share a stored video 3. B accepts video sharing 4. A put B voice call on hold 5. A retrieves B voice call 6. A invites B to share a stored video 7. B accepts video sharing |
| Expected results Post-conditions | 1. Voice call established between A and B. 2-3. Video sharing starts 4a. Voice call on hold 4b. Video sharing between A and B ends 4c. RCS capabilities are updated for A: image and Video Share services are no longer available 5. Voice call between A and B retrieved 6-7. Video sharing starts |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Video Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify session termination (sip/media) 5) Verify capability exchange following call on hold establishment (with B) and with B again when the call become active 6) Verify 1-4 for new session |

### Call waiting and Video Share

| Test case ID | RCS_8_1_4_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Call waiting. Users were in a CS call using Video Share. |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible |
| Test procedure | 1. A establishes a voice call with B 2. A invites B to share a stored video 3. B accepts video sharing 4. C calls A. A doesn't take the call |
| Expected results Post-conditions | 1. Voice call established between A and B. 2-3. Video sharing starts 4. Video sharing between A and B continues |
| Deep inspection | 1) Verify no impact from call waiting on to the current session |

### Multi-device handling

| Test case ID | RCS_8_1_5_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | A shares video with B ; B is using 2 devices |
| Pre-conditions Scenario | 1) B has 2 devices, B1 and B2, both online and active 2) A and B are in an active voice call; B is using his B1 device 3) Capabilities exchange has taken place confirming Video Share is possible 4) Both devices have front or rear facing camera |
| Test procedure | After the voice call is established, A starts Video Share to B B accepts the invite using his B2 device. A sends video to B; Video can be a pre-stored (stream) or live (camera[s]). |
| Expected results Post-conditions | B receives the video at his B2 device No more sharing capabilities available for A |
| Deep inspection | 1) Verify share session establishment (including INVITE forking and SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) Verify H.264 support in SDP negotiation |

### Exception conditions

| Test case ID | RCS_8_1_6_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | B rejects Video Share invite |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | B rejects A’s invite to live Video Share. It is not possible for A to start sharing. Handset A initiates a capability exchange to verify B status |
| Expected results Post-conditions | The call remains without Video Share |
| Deep inspection | 1) Verify signalling flow (invite+rejection) 2) Verify options exchange following cancelation (capability update) |

| Test case ID | RCS_8_1_6_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | A terminates voice call during ongoing Video Share |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) A is currently sharing a video with B (currently transferring) |
| Test procedure | A ends the call while sharing. |
| Expected results Post-conditions | The Video Share is terminated (video no longer displayed) |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) If a video session, verify H.264 support in SDP negotiation 5) Verify RTCP always used 6) Verify dummy packets sent |

| Test case ID | RCS_8_1_6_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | A cancels Video Share invite before B accepts |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Video Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | A sends Video Share invite to B but then decides to cancel it. B gets notification that the Video Share invite has been cancelled. Handset B verifies capabilities |
| Expected results Post-conditions | The call remains without Video Share |
| Deep inspection | 1) Verify invitation process 2) Verify cancelation response |

| Test case ID | RCS_8_1_6_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Graceful termination of Video Share session due to changing coverage |
| Pre-conditions Scenario | 1) A and B are in 3G coverage and in an active voice call 2) A Video Share session is already in place from A to B |
| Test procedure | B goes to 2G coverage, consequently, the Video Share session cannot be maintained. A stops sending video to B |
| Expected results Post-conditions | A stops receiving the video from B. |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) If a video session, verify H.264 support in SDP negotiation |

| Test case ID | RCS_8_1_6_5 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Non-graceful termination – receiver |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2)There is an active Video Share session from A to B |
| Test procedure | B goes out of coverage, therefore, the video send from A fails to reach B. Handset A performs a capability exchange to verify the new status |
| Expected results Post-conditions | The Video Share is terminated on both ends and the Video Share capability is shown as unavailable |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Video Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify RTP RR/timeout process 5) Verify signalling/media termination 6) Verify capability exchange following the event |

| Test case ID | RCS_8_1_6_6 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Video Share |
| Purpose | Non-graceful termination – sender |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2)There is an active Video Share session from A to B |
| Test procedure | A goes out of coverage, therefore, B stops receiving the video. Handset B performs a capability exchange to verify the new status |
| Expected results Post-conditions | The Video Share is terminated on both ends and the Video Share capability is shown as unavailable |
| Deep inspection | 1) Verify graceful establishment of the Video Share session (signalling) via traces (active session) and cancellation of the other invitation 2) Verify graceful establishment of the Video Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify RTP RR/timeout process 5) Verify signalling/media termination 6) Verify capability exchange following the event |

## Image Share

### Basic Image Share

| Test case ID | RCS_8_2_1_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Image Share, two simultaneous sessions |
| Pre-conditions Scenario | 1) A and B are in a voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1. A invites B to receive a stored picture 2. B accepts 3. B invites A to receive a stored picture 4. A accepts |
| Expected results Post-conditions | 1. Update capabilities for both users 2. picture sharing starts. B can see picture sent by A 3. picture sharing starts. A can see picture sent by B |
| Deep inspection | For each session: 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces |

| Test case ID | RCS_8_2_1_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Two sessions invitations at the same time |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | 1. A invites B to receive a stored picture. Before B accepts B invites A to receive another stored picture 2. B accepts 3. A accepts |
| Expected results Post-conditions | 1. Update capabilities for both users 2. Picture sharing starts. B can see picture sent by A 3. Picture sharing starts. A can see picture sent by B |
| Deep inspection | For each session: 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces |

| Test case ID | RCS_8_2_1_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Two simultaneous sessions. A does NOT accept |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1. A invites B to receive a stored picture 2. B accepts 3. B invites A to receive a stored picture 4. A does NOT accepts |
| Expected results Post-conditions | 1. Update capabilities for both users 2. Picture sharing starts. B can see picture sent by A 4. B receives an error message, as A rejects the invitation |
| Deep inspection | For successful session: 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces For non-successful session: 1) Verify invitation 2) Verify cancellation process |

### Multiparty call and Image Share

| Test case ID | RCS_8_2_2_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | A, B and C are in a CS call using Image Share (transfer not completed). |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1. A invites B to share a stored picture 2. B accepts picture sharing 3. A establishes a multiparty call with Users B and C |
| Expected results Post-conditions | 1. Voice call established between A and B. 2-3. Picture sharing starts 4a. Multiparty call is established among A, B and C 4b. Picture sharing between A and B is completed 4c. RCS capabilities are updated for A |
| Deep inspection | 1) Verify graceful establishment of the Image Share session (signalling) via traces (active session) 2) Verify graceful establishment of the Image Share session (media) via traces (active session) 3) Verify H.264 support in SDP negotiation 4) Verify session termination (sip/media) 5) Verify capability exchange following multiparty call establishment |

### Call on hold and Image Share

| Test case ID | RCS_8_2_3_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Call termination after transfer completed |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) A is currently sharing an image with B (the image had been already transferred and is still being displayed) |
| Test procedure | A ends the call |
| Expected results Post-conditions | The Image Share is terminated (image no longer displayed) |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) If a video session, verify H.264 support in SDP negotiation |

### Multi-device handling

| Test case ID | RCS_8_2_4_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | A shares image with B ; B is using 2 devices |
| Pre-conditions Scenario | B has 2 devices, B1 and B2, both online and active A and B are in an active voice call; B is using his B1 device Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | After the voice call is established, A starts Image Share, using stored image, to B B accepts the invite using his B2 device. A transfers the stored image to B |
| Expected results Post-conditions | B receives the image at his B2 device No more sharing capabilities available for A |
| Deep inspection | 1) Verify share session establishment (including INVITE forking and SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces |

### Exception conditions

| Test case ID | RCS_8_2_5_1 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | B rejects Image Share session offer |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible 3) Both devices have front or rear facing camera |
| Test procedure | 1) A invites B to receive a stored picture 2) B does NOT accept session offer |
| Expected results Post-conditions | 1. Update capabilities for both users, if applicable 2. Picture sharing doesn't start 3. A receives a message indicating "No answer" or similar after answer timeout expires. |
| Deep inspection | 1) Verify invitation process 2) Verify invitation timeout |

| Test case ID | RCS_8_2_5_2 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | A terminates voice call after image transfer completed |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) A is currently sharing an image with B (the image had been already transferred and is still being displayed) |
| Test procedure | A ends the call |
| Expected results Post-conditions | The Image Share is terminated (image no longer displayed) |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) If a video session, verify H.264 support in SDP negotiation |

| Test case ID | RCS_8_2_5_3 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | A terminates voice call during ongoing image transfer |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) A is currently sharing an image with B (currently transferring) |
| Test procedure | A ends the call while sharing. |
| Expected results Post-conditions | The Image Share is terminated (transfer cancelled) |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify graceful termination of the share session (signalling) via traces 3) Verify graceful termination of the share session (media) via traces 4) If a video session, verify H.264 support in SDP negotiation |

| Test case ID | RCS_8_2_5_4 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | A cancels Image Share invitation before B accepts |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1) A invites B to receive a stored picture 2) A send cancellation before B accepts |
| Expected results Post-conditions | 1. Update capabilities for both users, if applicable 2a. Picture sharing doesn't start 2b. B receives cancellation notification |
| Deep inspection | 1) Verify invitation process 2) Verify invitation cancelation |

| Test case ID | RCS_8_2_5_5 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | A cancels Image Share while image transfer is in progress |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1. A invites B to receive a stored picture 2. B accepts invitation 2. A send cancellation while sharing |
| Expected results Post-conditions | 1. Update capabilities for both users, if applicable 2. Picture sharing starts 3a. Picture sharing ends 3b. B receives cancellation notification |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify MSRP/session cancellation and session settlement 3) Verify options exchange following failure |

| Test case ID | RCS_8_2_5_6 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Image Share cancelled, B is no longer available |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1. A invites B to receive a picture 2. B accepts the invitation 3. B’sdevice is turned off, e.g., due to exhausted battery. |
| Expected results Post-conditions | 1. Update capabilities for both users, if applicable 2. image sharing starts (transfer) 3. the transfer is interrupted; both users are notified |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify MSRP/session timeout and session settlement 3) Verify options exchange following failure |

| Test case ID | RCS_8_2_5_7 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Non graceful termination due to lack of coverage |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible |
| Test procedure | 1. A invites B to receive a stored picture 2. B accepts 3. A loses all kind of coverage during transfer |
| Expected results Post-conditions | 1. Update capabilities for both users, if applicable 2. Picture sharing starts 3. Picture sharing ends |
| Deep inspection | 1) Verify share session establishment (including SDP negotiation) 2) Verify MSRP/session timeout and session settlement 3) Verify options exchange following failure (?) |

| Test case ID | RCS_8_2_5_8 |
| --- | --- |
| Related test cases |  |
| Tested feature | CONTENT SHARING; Image Share |
| Purpose | Image Share size limit (receiver) |
| Pre-conditions Scenario | 1) A and B are in an active voice call 2) Capabilities exchange has taken place confirming Image Share is possible 3) A is configured to have a larger file size transfer limit than B |
| Test procedure | a) A selects to share an image with B b) A select a file larger than B maximum file size (part of the configuration) NOTE: To facilitate self-accreditation this test can be simulated |
| Expected results Post-conditions | a) The invitation is sent across to B b) B gets a warning with the only option to reject the session c) The invitation is rejected |
| Deep inspection | 1) Verify invitation is sent 2) Verify invitation rejection and session settlement |

# IP Voice and Video Call

## IP Voice Call

### Two-party IP Voice Call over NNI

| Test Case ID | RCS_9_1_1_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can originate an IP Voice call that is terminated as an IP Voice call |
| Pre-conditions Scenario | A and B are in RCS-VoLTE mode or RCS-VoHSPA |
| Test procedure | A initiates an IP Voice call with B B answers the IP Voice call from A A ends the IP Voice call with B |
| Expected results Post-conditions | A two-party IP Voice call is successfully initiated, connected and ended between A and B. |
| Deep inspection | Verify establishment of the IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_1_2 |
| --- | --- |
| Related Test Cases | RCS_9_1_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can originate an IP Voice call that is terminated as a CS call. |
| Pre-conditions Scenario | A is in RCS-VoLTE or RCS-VoHSPA modes B is in RCS-CS mode B’s network terminates the IP Voice call as a CS call. |
| Test procedure | A initiates an IP Voice call with B B answers voice call from A A ends voice call with B |
| Expected results Post-conditions | A two-party IP Voice/CS voice call is successfully initiated, connected and ended between A and B. |
| Deep inspection | Verify establishment of the IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_1_3 |
| --- | --- |
| Related Test Cases | RCS_9_1_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can originate an IP Voice call that is terminated as a RCS IP Voice call. |
| Pre-conditions Scenario | A is in RCS-VoLTE or RCS-VoHSPA modes B is in RCS-CS or RCS-AA modeNote: B’s network terminates the IP Voice call as a RCS IP Voice call. |
| Test procedure | A initiates a IP Voice call with B B answers voice call from A A ends voice call with B |
| Expected results Post-conditions | A two-party IP Voice/RCS IP Voice call is successfully initiated, connected and ended between A and B. |
| Deep inspection | Verify establishment of the IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_1_4 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can place a IP Voice call on hold |
| Pre-conditions Scenario | A and B are on an active two-party IP Voice call A and B are in RCS-VoLTE mode |
| Test procedure | A places call on hold A resumes call B places call on hold B resumes call |
| Expected results Post-conditions | A two-party IP Voice call is successfully placed on and off hold by both parties |
| Deep inspection | Verify conformance with 3GPP TS 24.610 |

| Test case ID | RCS_9_1_1_5 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can originate a two-party RCS IP Voice call |
| Pre-conditions Scenario | A and B are in RCS-CS or RCS-AA modes |
| Test procedure | A initiates a RCS IP voice call with B B accepts voice call from A A ends voice call with B |
| Expected results Post-conditions | A two-party RCS IP voice call is successfully initiated, connected and ended between A and B. |
| Deep inspection | Verify establishment of the RCS IP voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_1_6 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can place an active RCS IP Voice call on hold |
| Pre-conditions Scenario | A and B are on an active two-party RCS IP Voice call A and B are in RCS-CS or RCS-AA modes |
| Test procedure | A places call on hold A resumes call B places call on hold B resumes call |
| Expected results Post-conditions | A two-party RCS IP Voice call is successfully placed on and off hold by both parties |
| Deep inspection | Verify conformance with 3GPP TS 24.610 |

| Test case ID | RCS_9_1_1_7 |
| --- | --- |
| Related Test Cases | RCS_9_1_1_5 first |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can originate a RCS IP Voice call that is terminated as a CS call |
| Pre-conditions Scenario | A is in RCS-CS or RCS-AA modes B is in RCS-CS mode |
| Test procedure | A initiates a RCS IP voice call with B B network terminates the call as a CS call to B B answers voice call from A A ends voice call with B |
| Expected results Post-conditions | A RCS IP Voice call is successfully initiated, connected and ended between A and B. |
| Deep inspection | Verify establishment of the RCS IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_1_8 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can originate a RCS IP Voice call that is terminated as a VoLTE call |
| Pre-conditions Scenario | A is in RCS-CS or RCS-AA mode B is in RCS-VoLTE or RCS-VoHSPA modes B network terminates the call as a VoLTE call to B |
| Test procedure | A initiates a RCS IP voice call with B B answers voice call from A A ends voice call with B |
| Expected results Post-conditions | A RCS IP voice call is successfully initiated, connected and ended between A and B. |
| Deep inspection | Verify establishment of the RCS IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_1_9 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can ignore an inbound IP Voice call |
| Pre-conditions Scenario | All users are in RCS-VoLTE or RCS-VoHSPA modes Note: voicemail service does not exist for B |
| Test procedure | A initiates an IP Voice call with B B ignores inbound call from A (no answer) |
| Expected results Post-conditions | An ignored two-party IP voice call between A and B is cancelled. |
| Deep inspection | Verify IP Voice call between A and B via traces was not established (i.e. 408 or 487 error response occurs) Verify attempted establishment of the IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session termination between A and C via traces |

| Test case ID | RCS_9_1_1_10 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can ignore an inbound RCS IP Voice call |
| Pre-conditions Scenario | A and B are visible and available on all devices All users are in RCS-CS or RCS-AA modes Note: voicemail service does not exist for B |
| Test procedure | A initiates an RCS IP Voice call with B B ignores inbound RCS IP Voice call from A (no answer) |
| Expected results Post-conditions | An ignored two-party RCS IP voice call between A and B is cancelled. |
| Deep inspection | Verify IP Voice call between A and B via traces was not established (i.e. 408 or 487 error response occurs) Verify attempted establishment of the RCS IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE |

| Test case ID | RCS_9_1_1_11 |
| --- | --- |
| Related Test Cases | List tests |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Validate the RCS client can ignore an inbound RCS IP Voice call during a two-party RCS IP call |
| Pre-conditions Scenario | All users are in RCS-CS or RCS-AA modes A and B are on an active RCS IP Voice call Note: voicemail service does not exist for A |
| Test procedure | C initiates an RCS IP Voice with A A ignores inbound call from C (no answer) |
| Expected results Post-conditions | A two-party RCS IP voice call between A and B is maintained and the call from C to A is cancelled. |
| Deep inspection | Verify IP Voice call between C and A via traces was not established (i.e. 408 or 487 error response occurs) Verify attempted establishment of the RCS IP Voice call between C and A via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE |

### Multi-party RCS Voice Call over NNI

| Test case ID | RCS_9_1_2_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Verify a RCS client can make a multi-party IP Voice call |
| Pre-conditions Scenario | A and B users are in RCS-VoLTE or RCS-VoHSPA modes C is a RCS user but not registered via IMS Note: C’s Network breaks out the IP Voice call to CS |
| Test procedure | A initiates a multiparty IP Voice call with B and C A ends IP Voice call with B and C |
| Expected results Post-conditions | A IP Voice multi-party call is successfully established and ended between A, B, and C. |
| Deep inspection | Verify establishment of the RCS IP Voice call session between A, B and C via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

| Test case ID | RCS_9_1_2_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Voice Call |
| Purpose | Verify a RCS client can make a multi-party RCS IP Voice call |
| Pre-conditions Scenario | A and B users are in RCS-CS or RCS-AA modes C is a RCS user but not registered via IMS Note: C’s Network breaks out the RCS IP Voice call to CS |
| Test procedure | A initiates a multiparty RCS IP Voice call with B and C A ends RCS IP Voice call with B and C |
| Expected results Post-conditions | A RCS IP Voice multi-party call is successfully established and ended between A, B, and C. |
| Deep inspection | Verify establishment of the RCS IP Voice call session between A, B and C via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE Verify session terminations via traces |

## IP Video call

### Two-party IP Video call over NNI

| Test case ID | RCS_9_2_1_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can originate a two-party IP Video call |
| Pre-conditions Scenario | A and B are IP Video call capable All users are in RCS-VoLTE or RCS-VoHSPA Mode Capabilities exchange has taken place confirming video calling is possible All devices have a front or rear facing camera |
| Test procedure | A initiates a IP Video call with B B answers IP Video call from A Video call between A and B ends |
| Expected results Post-conditions | A two-party IP Video call is initiated and successfully ends between A and B. |
| Deep inspection | Verify establishment of the IP Video call via traces Verify SIP: P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” Accept-Contact and Contact header fields containing the “video” capability indication and audio and video media in SDP in 200 OK response Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria Verify session terminations via traces |

| Test case ID | RCS_9_2_1_2 |
| --- | --- |
| Related Test Cases | RCS_9_2_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can place a two-party IP Video call on hold |
| Pre-conditions Scenario | A and B are in an active two-party IP Video call All users are in RCS-VoLTE or RCS-VoHSPA mode |
| Test procedure | A places IP Video call on hold A resumes IP Video call B places IP Video call on hold B resumes IP Video call |
| Expected results Post-conditions | A two-party IP Video call is successfully placed on and off hold by both parties |
| Deep inspection | Verify conformance with 3GPP TS 24.610 |

| Test case ID | RCS_9_2_1_3 |
| --- | --- |
| Related Test Cases | RCS_9_2_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can ignore an inbound IP Video call |
| Pre-conditions Scenario | A and B are IP Video call capable All users are in RCS-VoLTE or RCS-VoHSPA Mode Capabilities exchange has taken place confirming video calling is possible All devices have a front or rear facing camera Voice/Video mail service is inactive for B |
| Test procedure | A initiates an IP Video call with B B ignores inbound call from A (no answer) |
| Expected results Post-conditions | An ignored two-party IP Video call between A and B is cancelled. |
| Deep inspection | Verify IP Video call between A and B via traces was not established (i.e. 408 or 487 error response occurs) |

| Test case ID | RCS_9_2_1_4 |
| --- | --- |
| Related Test Cases | RCS_9_2_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can accept only IP Voice from a inbound IP Video call |
| Pre-conditions Scenario | A and B are IP Video call capable All users are in RCS-VoLTE or RCS-VoHSPA Mode Capabilities exchange has taken place confirming video calling is possible All devices have a front or rear facing camera |
| Test procedure | A initiates an IP Video call with B B accepts inbound IP Voice from A |
| Expected results Post-conditions | A rejected two-party IP Video call between A and B successfully connects as an IP Voice call. |
| Deep inspection | Verify establishment of the IP Voice vs. IP Video call between A and B via traces Verify SIP INVITE: P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” Accept-Contact and Contact header fields containing the “video” capability indication and audio and video media in SDP in 200 OK response |

| Test case ID | RCS_9_2_1_5 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate two-party IP Video call can gracefully degrade due to changing conditions |
| Pre-conditions Scenario | Active IP Video call between A and B All devices have a front or rear facing camera |
| Test procedure | B moves into 3G coverage, consequently, the two-party video session cannot be maintained. |
| Expected results Post-conditions | B stops sending video to A or receiving video from A The voice session downgrades to a CS call |
| Deep inspection | Verify video portion of the IP Video call between A and B was removed via traces Verify graceful termination of the two-party video session and establishment of a CS call via traces |

| Test case ID | RCS_9_2_1_6 |
| --- | --- |
| Related Test Cases | RCS_9_1_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate a two-party IP Video call can be downgraded to IP Voice Call |
| Pre-conditions Scenario | Active IP Video call between A and B All devices have a front or rear facing camera |
| Test procedure | Video session is cancelled by A or B during an active IP Video call. IP Video call degrades to a IP Voice call between A and B. |
| Expected results Post-conditions | A two-party IP Video call degrades to a two-party IP Voice call between A and B. |
| Deep inspection | Verify video portion of the IP Video call between A and B was removed via traces |

| Test case ID | RCS_9_2_1_7 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can upgrade an active two-party IP Voice call to a two-party IP Video call |
| Pre-conditions Scenario | A and B are IP Video call capable All users are in RCS-VoLTE or RCS-VoHSPA Mode Capabilities exchange has taken place confirming video calling is possible All devices have a front or rear facing cameraActive IP Voice call between A and B |
| Test procedure | A later upgrades IP Voice call to an IP Video call with B B accepts IP Video call from A |
| Expected results Post-conditions | A two-party IP Voice call is upgraded to a two-party IP Video call between A and B. |
| Deep inspection | Verify SIP REINVITE: P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” Accept-Contact and Contact header fields containing the “video” capability indication and audio and video media in SDP in 200 OK response Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria |

| Test case ID | RCS_9_2_1_8 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can originate a two-party RCS IP Video call |
| Pre-conditions Scenario | A and B are RCS IP Video call capable All users are in RCS-CS or RCS-AA Mode Capabilities exchange has taken place confirming video calling is possible All devices have a front or rear facing camera |
| Test procedure | A initiates a RCS IP Video call with B B answers RCS IP Video call from A |
| Expected results Post-conditions | A two-party RCS IP Video call is initiated between A and B. |
| Deep inspection | Verify establishment of the video session via traces Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” Accept-Contact and Contact header fields containing the “video” capability indication and audio and video media in SDP in 200 OK response Separate RTP streams for audio and video in session established using SIP INVITE Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria |

| Test case ID | RCS_9_2_1_9 |
| --- | --- |
| Related Test Cases | RCS_9_2_1_1 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can place a two-party RCS IP Video call on hold |
| Pre-conditions Scenario | A and B are in an active two-party RCS IP Video call All users are in RCS-CS or RCS-AA mode |
| Test procedure | A places RCS IP Video call on hold A resumes RCS IP Video call B places RCS IP Video call on hold B resumes RCS IP Video call |
| Expected results Post-conditions | A two-party RCS IP Video call is successfully placed on and off hold by both parties |
| Deep inspection | Verify conformance with 3GPP TS 24.610 |

| Test case ID | RCS_9_2_1_10 |
| --- | --- |
| Related Test Cases | RCS_9_2_1_8 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can upgrade a two-party CS Voice call to a two-party RCS IP Video call, make before break |
| Pre-conditions Scenario | A and B are RCS IP Video call capable All users are in RCS-CS mode Capabilities exchange has taken place confirming voice and video calling is possible A and B are on an active two-party CS voice call All devices have a front or rear facing camera |
| Test procedure | A initiates a RCS IP video call with B B accepts RCS IP Video call from A |
| Expected results Post-conditions | A two-party CS voice call is migrated to a two-party RCS IP Video call and successfully ends between A and B. |
| Deep inspection | Verify CS voice call between A and B ends after B accepts RCS IP Video call Verify establishment of the IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” Accept-Contact and Contact header fields containing the “video” capability indication and audio and video media in SDP in 200 OK response Separate RTP streams for audio and video in session established using SIP INVITE Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria |

| Test case ID | RCS_9_2_1_11 |
| --- | --- |
| Related Test Cases | RCS_9_2_1_8 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can upgrade a two-party CS Voice call to a two-party RCS IP Video call, break before make |
| Pre-conditions Scenario | A and B are RCS IP Video call capable All users are in RCS-CS mode Capabilities exchange has taken place confirming voice and video calling is possible A and B are on an active two-party CS voice call All devices have a front or rear facing camera |
| Test procedure | A initiates a RCS IP Video call with B B accepts video call from A |
| Expected results Post-conditions | A two-party CS voice call is migrated to a two-party RCS IP Video call and successfully ends between A and B. |
| Deep inspection | Verify CS voice call between A and B ends before B accepts RCS IP Video call Verify establishment of the IP Voice call between A and B via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” Accept-Contact and Contact header fields containing the “video” capability indication and audio and video media in SDP in 200 OK response Separate RTP streams for audio and video in session established using SIP INVITE Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria |

| Test case ID | RCS_9_2_1_12 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client can reject a two-party IP Video call upgrade request from a two-party IP Voice call |
| Pre-conditions Scenario | A and B are IP Video call capable All users are in RCS-VoLTE or RCS-VoHSPA Mode Capabilities exchange has taken place confirming video calling is possible All devices have a front or rear facing camera Active IP Voice call between A and B |
| Test procedure | B later attempts to upgrade IP Voice call to a IP Video call with A A rejects the IP Video call upgrade from B IP Voice call continues between A and B |
| Expected results Post-conditions | A two-party IP Voice call is not upgraded to a two-party IP Video call and the IP Voice call continues between A and B. |
| Deep inspection | Verify IP Video call upgrade between A and B failed via traces (i.e. 488 error response occurs) |

| Test case ID | RCS_9_2_1_13 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Video Muting |
| Pre-conditions Scenario | A and B are in an active IP video call All users are in RCS-VoLTE mode |
| Test procedure | A selects a video mute toggle via the application UI. A suspends the video data transmission to B. A selects the video mute toggle via the application UI. A resumes the video data transmission to B. |
| Expected results Post-conditions | A stops sending video RTP packets to B. A keeps sending RTCP Sender reports to B with zero bytes to indicate that A has muted the RTP stream(s). A resumes sending video RTP packets to B. A sends RTCP Sender reports to B with appropriate byte count to indicate that A has stopped muting the RTP stream(s) |
| Deep inspection | Verify no video RTP packets are sent Verify A keeps sending RTCP Sender reports to B with zero bytes for the muted the RTP stream(s). Verify video RTP packets are sent Verify A keeps sending RTCP Sender reports to B with appropriate byte count for the video RTP stream(s). |

| Test case ID | RCS_9_2_1_14 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client cannot make a two-party RCS IP Voice call to a RCS IP Video call only device; RCS IP Voice call fails |
| Pre-conditions Scenario | A and B are RCS IP Video call capable (B is a RCS IP Video Call Only device; B is not RCS IP Voice call capable) All users are in RCS-CS or RCS-AA modes Capabilities exchange has taken place confirming voice and/or video calling is possible All devices have a front or rear facing camera |
| Test procedure | A initiates a RCS IP Voice call with B) B phone does not ring RCS IP Voice call fails |
| Expected results Post-conditions | A two-party RCS IP Voice call to a RCS IP Video Only device fails. |
| Deep inspection | Verify IP Voice call between A and B fails via traces (i.e. 488 error response occurs |

| Test case ID | RCS_9_2_1_15 |
| --- | --- |
| Related Test Cases | RCS_9_1_1_7 |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate the RCS client cannot make a two-party RCS IP Voice call to a RCS IP Video call only device; RCS IP Voice Call break out by terminating network |
| Pre-conditions Scenario | A and B are RCS IP Video call capable (B is a RCS IP Video Call Only device; B is not RCS IP Voice call capable) All users are in RCS-CS or RCS-AA modes Capabilities exchange has taken place confirming voice and/or video calling is possible All devices have a front or rear facing camera Terminating network breaks out RCS IP Voice calls to CS call to devices with video only restriction |
| Test procedure | A initiates a RCS IP Voice call with B B answers CS call |
| Expected results Post-conditions | A RCS IP Voice call is successfully terminated as a CS call. |
| Deep inspection | Verify establishment of the RCS IP Voice session over the NNI via traces Note: UE and networks follow 3GPP TS 24.229, 3GPP TS 24.173 and 3GPP TS 26.114 for establishment and termination of a call Verify: SIP INVITE P-Asserted-Service: urn:urn-7:3gpp-service.ims.icsi.mmtel.gsma.ipcall Accept-Contact and Contact header fields containing the feature tag +g.3gpp.icsi-ref="urn%3Aurn-7%3A3gpp-service.ims.icsi.mmtel” and only audio media in SDP in 200 OK response RTP in session established using SIP INVITE |

| Test case ID | RCS_9_2_1_16 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate call failure when a RCS client only accepts IP Voice from a IP Video call only device |
| Pre-conditions Scenario | A and B are RCS IP Video call capable (A is a RCS IP Video Call Only device; A is not RCS IP Voice call capable) All users are in RCS-CS or RCS-AA modes Capabilities exchange has taken place confirming voice and/or video calling is possible All devices have a front or rear facing camera |
| Test procedure | A initiates a RCS IP Video call with B B phone rings B Accepts RCS IP Voice RCS IP Video call fails |
| Expected results Post-conditions | A two-party RCS IP Video Call fails when video is not accepted by a non-video only restricted device. |
| Deep inspection | Verify A device/network terminates the call when B only accepts RCS IP Voice |

### Multi-party RCS Video call over NNI

| Test case ID | RCS_9_2_2_1 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate multi-party IP Video call capability |
| Pre-conditions Scenario | A and B are IP Video call capable All users are in RCS-VoLTE mode Capabilities exchange has taken place confirming video calling is possible Active IP Video call between A and B All devices have a front or rear facing camera |
| Test procedure | A initiates a multiparty IP Video call with B and C |
| Expected results Post-conditions | Multi-party IP Video calls are successfully initiated between A, B, and C. |
| Deep inspection | Verify session setup via traces Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria |

| Test case ID | RCS_9_2_2_2 |
| --- | --- |
| Related Test Cases |  |
| Feature | IP VOICE AND VIDEO CALL; IP Video Call |
| Purpose | Validate multi-party RCS IP Video call capability |
| Pre-conditions Scenario | A and B are RCS IP Video call capable All users are in RCS-CS or RCS-AA mode Capabilities exchange has taken place confirming video calling is possible Active RCS IP Video call between A and B All devices have a front or rear facing camera |
| Test procedure | A initiates a multiparty RCS IP Video call with B and C |
| Expected results Post-conditions | Multi-party RCS IP Video call are successfully initiated between A, B, and C. |
| Deep inspection | Verify session setup via traces Verify H.264 support in SDP negotiation (pre-condition) If Video call is with a front feed camera, verify lip synchronization complies with minimum performance criteria |

# Personal Network Blacklist

## Standalone Message

### Standalone message (Pager Mode) is screened out in terminating network

| Test case ID | RCS_10_1_1_1 |
| --- | --- |
| Related test case(s) | test case ID for Send Pager Mode message 1-to-1 |
| Feature tested | Personal Network Blacklist; Standalone Message; |
| Purpose | Validate standalone message (Pager Mode) being screened out from terminating network. |
| Pre-conditions Scenario | 1. Both A and B is capable of standalone messaging. 2. The operators of both A and B have NNI interoperability of Personal Network Blacklist. 3. A is among the blacklisted users list ‘rcs_pnb_standalone_blockedusers’ of B in the Blacklist Policy Enforcement Function (BPEF). |
| Test procedure | 1. A initiates the sending of a standalone message in Pager Mode, with 100 bytes of content, towards B. |
| Expected results Post-conditions | 1. The standalone message is not delivered to B as the BPEF of terminating network determines that the delivery of the standalone message is to be blocked. 2. Verify no standalone message delivery and/or display notifications will be returned to A if such delivery and/or display notifications are requested by A. |
| Deep inspection | 1. Verify SIP MESSAGE request is sent from A network to B network and the P-Asserted- Identity header field does contain A’s SIP URI. 2. Verify a SIP 403 Forbidden response is received in the originating network with a warning header set to “122 Function not allowed”. |

### Standalone message (Large Message Mode) is screened out in terminating network

| Test case ID | RCS_10_1_2_1 |
| --- | --- |
| Related test case(s) | test case ID for Send Large Message Mode message 1-to-1 |
| Feature tested | Personal Network Blacklist; Standalone Message; |
| Purpose | Validate the SIP error code returned for standalone message (Large Message Mode) being screened out from terminating network. |
| Pre-conditions Scenario | 1. Both A and B is capable of standalone messaging. 2. The operators of both A and B have NNI interoperability of Personal Network Blacklist. 3. A is among the blacklisted users list ‘rcs_pnb_standalone_blockedusers’ of B in the Blacklist Policy Enforcement Function (BPEF). |
| Test procedure | 1. A initiates the sending of a standalone message in Large Message Mode, with more than 1300 bytes of content, towards B. |
| Expected results Post-conditions | 1. The standalone message is not delivered to B as the BPEF of terminating network determines that the delivery of the standalone message is to be blocked. 2. Verify no standalone message delivery and/or display notifications will be returned to A if such delivery and/or display notifications are requested by A. |
| Deep inspection | 1. Verify SIP INVITE request is sent from A network to B network and the P-Asserted- Identity header field does contain A’s SIP URI. 2. Verify a SIP 403 Forbidden response is received in the originating network with a warning header set to “122 Function not allowed”. |

## Chat Session

### Chat (1-to-1) invitation is screened out in terminating network

| Test case ID | RCS_10_2_1_1 |
| --- | --- |
| Related test case(s) | test case ID for 1-to-1 Chat |
| Feature tested | Personal Network Blacklist; Chat Session ; |
| Purpose | Validate 1-to-1 Chat session invitation being screened out from terminating network. |
| Pre-conditions Scenario | 1. Both A and B is capable of chat service. 2. The operators of both A and B have NNI interoperability of Personal Network Blacklist. 3. A is among the blacklisted users list ‘rcs_pnb_chat_blockedusers’ of B in the Blacklist Policy Enforcement Function (BPEF). |
| Test procedure | 1. A initiates 1-to-1 Chat session invitation towards B. |
| Expected results Post-conditions | 1. The Chat invitation is not delivered to B as the BPEF of terminating network determines that the delivery of the Chat invitation is to be blocked. 2. Verify no Chat message delivery and/or display notifications will be returned to A if such delivery and/or display notifications are requested by A. |
| Deep inspection | 1. Verify SIP INVITE request is sent from A network to B network and the P-Asserted- Identity header field does contain A’s SIP URI. 2. Verify a SIP 403 Forbidden response is received in the originating network with a warning header set to “122 Function not allowed”. |

## File Transfer

### File Transfer invitation is screened out in terminating network

| Test case ID | RCS_10_3_1_1 |
| --- | --- |
| Related test case(s) | test case ID for Basic File Transfer (MSRP) |
| Feature tested | Personal Network Blacklist; File Transfer ; |
| Purpose | Validate MSRP-based File Transfer session invitation being screened out from terminating network. |
| Pre-conditions Scenario | 1. Both A and B is capable of MSRP-based file transfer service. 2. The operators of both A and B have NNI interoperability of Personal Network Blacklist. 3. A is among the blacklisted users list ‘rcs_pnb_ft_blockedusers’ of B in the Blacklist Policy Enforcement Function (BPEF). |
| Test procedure | 1. A initiates MSRP-based File Transfer invitation towards B. |
| Expected results Post-conditions | 1. The File Transfer invitation is not delivered to B as the BPEF of terminating network determines that the delivery of the File Transfer invitation is to be blocked. The File Transfer session is not established with B. |
| Deep inspection | 1. Verify SIP INVITE request is sent from A network to B network and the P-Asserted- Identity header field does contain A’s SIP URI. 2. Verify a SIP 403 Forbidden response is received in the originating network with a warning header set to “122 Function not allowed”. |

# Document Management

## Document History

| Version | Date | Brief Description of Change | Approval Authority | Editor / Company |
| --- | --- | --- | --- | --- |
| 0.1 | Jan 28 2013 | Initial version | RCC TF #56 | GSMA |
| 0.11 | Jan 30 2013 | Added Capability Exchange, Content Sharing |  | GSMA |
| 0.12 | Feb 2nd 2013 | Comments and test cases by Bipin Patel (BP) Test cases by Mike M Parsel |  | GSMA |
| 0.13 | Feb 5th | Test Cases by Randy Wohlert, AT&T (RW) Comments by Brian McColgan, RIM (bmc) Test case headings by Ning Yeh (NY) |  | GSMA |
| 014 | not released |  |  | GSMA |
| 0.15 | Feb 10th | Including input from review Feb 8th |  | GSMA |
| 0.20 | Feb 15th | Including input from review Feb 14th |  | GSMA |
| 0.21 | Feb 25th | Cleaned up 0.20 |  | GSMA |
| 0.22 | March 12th | Added Test Cases from Yet Chang (PNB) Modified IP Voice, IP Video Added architecture |  | GSMA |
| 0.30 | March 21st | Included Test Cases from Ning (Messaging) Included Test Cases by Michael Koester (File Transfer over http) Included comments from Jerry Shih to Chapter 6, 9 and 10 |  | GSMA |
| 0.31 | March 21st | Cleaned up 0.30 Consistent numbering |  | GSMA |
| 0.32 | March 22nd | Updated Chapter 11 PNB to v3 (YC) |  | GSMA |
| 0.40 | March 27th | Restructured 3, 5, 6.1, 8 |  | GSMA |
| 0.41 | March 31st | Updated Chapter 11 PNB to v3.1 (YC) Restructured 6.2 |  | GSMA |
| 0.42 | April Fool | Updated Chapter 7 Messaging Added multidevice tests for Video Share (8_1_5_1) and Image Share (8_2_4_1) |  | GSMA |
| 0.43 | April 3rd | Reviewed in RCSNTCM #5 |  | GSMA |
| 0.44 | April 3rd | Updated section 9 IP Voice/Video (former sections 9 and 10) Updated section 6.2 File Transfer over http (former section 6.5) Cleaned up 3.1 and 6.1 after review |  | GSMA |
| 0.45 | April 4th | Added 3 File Transfer TCs (6_5_1_x, _y, _z) Updated section 3.2 and 5 based on outcome of the review (Clint Banner) Updated Chapter 10 (former 11) on PNB (Yet Chang) |  | GSMA |
| 0.46 | April 6th | After final f2f review Updated 6_4_2x (FT/Exception Conditions) Updated Chapter 9 to “almost perfect” |  | GSMA |
| 0.47 | April 11th | Updated 6_1_5_x/y/z (Ning Yeh) Updated Chapter 7 (Ning Yeh) Updated Chapter 8 (Vlad D) |  | GSMA |
| 0.9 | April 14th | After final review |  | GSMA |
| 0.91 | April 15th | Updated 6.2 (M Koster) |  | GSMA |
| 1.0 | April 17th | Renumbered Released |  | GSMA |

## Other Information

| Type | Description |
| --- | --- |
| Document Owner | RCC TF |
| Editor / Company | Vladimir Durovic GSMA |

It is our intention to provide a quality product for your use. If you find any errors or omissions, please contact us with your comments. You may notify us at prd@gsm.org

Your comments or suggestions & questions are always welcome.